CUBE

(Small-C)

User Document

Date last modified: May 25, 2006

Author: Daniel S. Kim

Blank Page

Table of Content

1.	INTRODUCTION	7

2.	PURPOSE	7

3.	SCOPE	8

4.	IDE/SATA PCI controller supported	8

5.	Major Features Supported (Key features)	8

6.	REQUIREMENT	8

6.1.	UDMA:	9

7.	Setup	11

8.	Language Syntax (Small-C)	12

8.1.	RESERVED and KEY WORDs	12

8.2.	Variables, Constants, Operations, and Expressions	12

8.2.1.	Identifier Names	12

8.2.2.	Reserved Identifiers	13

8.2.3.	Data Types	13

8.2.4.	Declaration	13

	Global declaration	14

	Local declaration	14

8.2.5.	Variable Initializations	15

8.2.6.	Operators	15

	Arithmetic Operators	15

	Relation and Logical Operations	16

	Bitwise Operators	17

	Assignment statements	17

8.2.7.	Precedence and Order of Evaluation	18

8.2.8.	Expression & Statement	18

8.3.	Program Control Statements	18

8.3.1.	IF Statement	20

8.3.1.1.	IF	20

8.3.1.2.	IF-ELSE	20

8.3.1.3.	Nested IF Statement	20

8.3.2.	SWITCH Statement	21

8.3.3.	WHILE Statement	22

8.3.4.	 DO-WHILE Statement	22

8.3.5.	FOR Statement	22

8.4.	Function	24

8.4.1.	Pre-Defined Function	24

8.4.2.	User Defined Function	24

8.5.	Pre-processor (#include & #define)	25

8.5.1.	#include	25

8.5.2.	#define	25

9.	WCUBE	25

9.1.	Overview	25

9.2.	Features	26

9.3.	Device Configuration	28

9.4.	Text Editor Window/Main Window	31

9.4.1.	Overview	31

9.4.2.	The Interface	32

9.5.	The Command Line	35

9.5.1.	Overview	35

9.5.2.	The Interface	35

9.6.	Buffer Editor	37

9.6.1.	Overview	37

9.6.2.	The Interface	38

9.7.	Command History	40

9.8.	Disk Status	41

9.9.	Disk Info	41

9.10.	Flags	42

9.11.	Macros	43

9.12.	Notes on Compatibility Mode	44

9.13.	Known Issues and Notes	46

10.	The CUBE	47

10.1.	CUBE.INI file	48

10.2.	Macro support	49

10.3.	CUBE Built-in/Predefined Functions and Variables	51

10.3.1.	Predefined Variables	51

10.3.2.	Command-line Commands	52

10.3.3.	Console: Function Keys	53

10.3.4.	Edit	53

10.3.5.	Help	55

10.3.6.	Console: Basic I/O Functions	56

10.3.7.	Console: Display Functions	57

10.3.8.	Run-time Control Flag Switch	58

10.3.9.	Trace/Debug functions	59

10.3.10.	Buffer functions	60

10.3.10.1.	Bedit	61

10.3.11.	Power Control Functions	65

10.3.11.1.	ATX Power Control Via Parallel Port (PWR_CONTROL = 1)	66

10.3.12.	PCI functions	66

10.3.13.	Memory Mapped IO	67

10.3.14.	Other & Date/ Time	68

10.3.15.	Legacy Command Tag-Queue	69

10.3.16.	Native Command Queuing	70

10.3.17.	Drive Commands	72

10.3.18.	Drive Commands (Samsung VU Commands)	77

10.3.19.	MISC commands (Math,Test….)	80

10.3.20.	Command compatibility between Gemini and Cube	80

10.4.	Using CUBE	81

10.4.1.	Setting-up test environment by selecting the controller	82

10.4.2.	CUBE Test Script Examples	84

10.4.2.1.	Sequential Seek Time Measurement:	84

10.4.2.2.	Random Seek Time Measurement:	85

10.4.2.3.	Do Sequential DMA Write/Read:	86

10.4.2.4.	Do Sequential UDMA Write/Read:	87

10.4.2.5.	Legacy Command Queuing:	88

11.	VTOOL	88

11.1.	Overview	88

11.2.	Configuration	92

REVISION HISTORY

| Rev | Date | By | Comments |
| --- | --- | --- | --- |
| Alpha | 04/20/2004 | Daniel S. Kim |  |
| 1.00 | 11/29/04 | Nan K. Hall |  |
| 2.00 | 01/28/2005 | Derrick Chu |  |
| 2.01 | 02/11/2005 | Daniel S. Kim | Update Small-c changes |
| 2.02 | 01/27/2006 | Nan K. Hall |  |
| 2.03 | 05/25/2006 | Nan K. Hall | Adding file commands |

# INTRODUCTION

This documentation lays out the “Small-C” language definition.

Small-C is developed to serve as a generic test language for Samsung. Small-C has three major parts:

- Lexical Analyzer (or, tokenizer)

- Parser (Syntax analyzer based on Small-C grammar)

- Code generator

Of these three, Lexical Analyzer and Parser is a generic Small-C compiler components. The Code Generator in other hand is micro-processor specific. At the time of this write-up, the code we are generating is based on CUBE virtual – for Cube related topics, please refer to section 7.

In short, Small-C is a “C”-like language with some of the C features/syntaxes removed. Some of the key “C” features/syntaxes you will NOT see in “Small-C” are:

- being able to define structures

- enumerations

- pointers and pointer operations

- variable initialization as it is being defined

- ellipsis

In this documentation, I’ll attempt to describe the follow:

- Reserved words

- Language feature and syntax

- Small-C usage (inputs and outputs)

# PURPOSE

This document serves as a reference for those who require to write Small-C codes (script), the syntax and the grammar.

# SCOPE

This document is intended for the programmers developing Small-C based test codes.  For those who are doing a Small-C programming can skip the first few sections and move right into the language syntax section.

You’ll find 5 major sections in this document:

- Small-C grammer/syntax

- Cube (DOS version)

- WCube (Windows version)

- Command set

- VTool (embedded in WCube)

# IDE/SATA PCI controller supported

- All on-board PCI chipset should work in Compatible mode (some may also work in Native mode)

    - VIA, SiS, NVidia (Compat mode)

    - ICH4/5 systems (Compat & Native mode – BIOS configured)

    - Promise 100Tx2, 133Tx2 (Native mode)

    - Promise 33, 66, 100 (Native mode)

    - Si3124 – (to support NCQ)

      - Special note on Si3124 Driver:

        - *** When an error is detected during the drive command execution, the driver will clear the interrupt, then issue a reset to the card to get the card into a known good state. This will be done for the given channel only *** (for more info on this, see Si3124 technical document). An example of this situation is when an invalid command is issued to the drive.

# Major Features Supported (Key features)

- UDMA

- Stream command set (including DMA)

- Legacy command queuing (see sample script in Appendix section)

- Command History

- Advanced scripting (Small-C)

- Console functions for user defined screen (user can control the console screen)

- Command execution time measurement to microsecond accuracy

- Macro support

- PCI & related built in function support

- etc…

# REQUIREMENT

- Hardware:

  - PC (Pentium with 8meg or more memory)

  - Storage device (Floppy or resident HDD) – to store the program

  - HDD Controller

    - On-board PCI chipset (IDE/SATA controller) supported

      - All onboard PCI chipset should work in Compatible mode (some may also work Native mode)

      - Tested PCI Chipsets

        - VIA

        - SiS

        - NVidia

        - Intel (ICH4 / ICH5) – also can run in native mode

    - Promise PATA controller:

      - U33 (not tested)

      - U66 (not tested)

      - U100 - TESTED

      - U133 - TESTED

  - Optional:

    - Power control

      - Samsung ISA Power control board

      - ATX power supply with Parallel port connection

UDMA:

- Drive settings and info:

To see/verify that a particular udma mode has been set use the id command (id 1). This will display various information about the drive, including the udma mode of the drive. Near the bottom of the information you will see the udma mode:

CMD Defa[87]: 0x4003

Ultra DMA[88]: 0x7F

SCT CMD Supp : 0x0

To interpret the "Ultra DMA[88]" line, you need to understand that the displayed value is two bytes, any leading zeros are not displayed. So in the above case, the value we ought to see it as is 0x007F. The left byte (0x00) represents the udma mode that is set, and the right byte (0x7F) is what the drive supports.

To understand these values, we must convert the number into binary. To see what udma mode the drive supports we convert the right byte. Converting 0x7F to binary we get 01111111b. Label the bits right to left from zero (0) to seven (7). For each bit set represents that that udma mode is supported. So the right most bit at position zero (0)  means udma mode 0 is support, one bit to the left at position one (1) means udma mode 1 is supported, and so on a so forth.

Similarly we do the same for the left byte to see what udma mode is currently set. Converting 0x00 to binary we get 00000000b, so we see that no udma mode is set.

Here is another example. Say we do an "id 1" and we see:

Ultra DMA[88]: 0x43F

We convert the right byte to binary, 0x3F = 00111111b. This means that all only udma modes 5 to 0 are supported. And if we conver the left byte to binary, 0x04 = 00000100b, we see that the drive is currently operating in udma mode 2.

- How to set UDMA mode:

By default, the drive will be set to no dma mode. However, if the drive is plugged in while the system is booting, the drive will automatically be set to the highest DMA mode possible.

To set udma mode, you use the set features command (setf). setf takes a two byte argument. It is simplest to input the argument as a hexadecimal number as you will see why.

The generic command to set udma is:

setf(0x4?03)

where the question mark (?) represents the mode. So to set udma mode 4 you type:

setf(0x4403)

The left byte (0x4?) represents that you wish to set udma mode and which mode; the right byte (0x03) represents that you wish to set the transfer mode.

So the left four-? (0x4?) represents udma setting udma with the question mark signifying which mode. The right zero-three (0x03) represents setting the transfer mode.

If you attempt to set the drive to an invalid/non-supported udma mode, the drive will report an error. If you are unsure the set features command went through, type "id 1" and see what udma mode the drive is set at.

For more information regarding the set features command, refer to the ATA command spec.

- Limitations:

For (at least) Promise cards, if a drive is ever disconnected and reconnected, it is imperative that you set dma mode using the setf() command before issuing a dma command. Failure to do so may lead to system hang/freeze.

Additionally, for Promise cards, UDMA mode 5 and 6 are supported, with restrictions. To get the modes to work, you must have the drive plugged in while the system is booting. If no drive is connected at boot up and you try to set udma mode 5 or 6, you may recieve CRC errors. Once the system has booted, you may disconnect and reconnect a different drive if you wish, provided you set the udma mode again.

- Software:

  - Latest CUBE.EXE

  - Driver file (*.drv)

    - INT_ICH.DRV for ICH 4 or 5 (Native or Compat mode – BIOS controlled)

    - PRO_IDE.DRV for Promise U33/66/100/133 (Native mode)

    - Other on-board chipset (Compat mode)

  - TNT runtime library

  - OS (Dos)

  - Optional: Text Editor

# Setup

# Language Syntax (Small-C)

This section describes the Small-C language syntax and its usage.

## RESERVED and KEY WORDs

Following are the key and reserved words for Small-C language.

These words can not be used as a variable name in script files.

The following are Small-C generic reserved words

- break

- case

- char

- continue

- default

- do

- else

- float

- for

- goto

- if

- int

- return

- switch

- void

- while"

## Variables, Constants, Operations, and Expressions

Variables and constants are manipulated by operators to form expressions. These are the most basic elements of Small-C language. This section will closely examine each.

### Identifier Names

In Small-C, the names that are used to reference variables and labels are known as identifiers. The length of an identifier in Small-C can vary from one to several characters. In all cases the first character must be a letter, and subsequent characters must be either letters, numbers, or underscore. Here are some examples of correct and incorrect identifier names.

| Correct | Incorrect |
| --- | --- |
| num | 23num |
| myid23 | myid?23 |
| my_ident | my_ident? |
| my_float | my_float@ |
| my_str | my_str# |

The length of identifier is limited up to 200 characters.

There are two types of identifiers, user defined and reserved (Machine dependent/specific). Reserved identifiers are the variable names that are predefined for a machine that can be accessed by script file.

example:

void main(void)

{

int total;		// declare a variable of int

total = 1;

return;

}

### Reserved Identifiers

For the reserved identifier, see section 7.

### Data Types

In Small-C, there are three data types that are supported, and they are as follows:

| Type | Num of bytes | Comment |
| --- | --- | --- |
| char | 1 | Capable of holding one character |
| int | 4 | signed integer |
| float | 4 | signed single-precision floating point number |

### Declaration

All variables must be declared before use. A declaration specifies a type, and is followed by a list of one or more variables of that type.

Example:

char		mychar;		// declare mychar

float		taxRate, total;	// Declare taxRate & total

Declaration can be either GLOBAL or LOCAL

You can not re-declare Reserved or Key words.

#### Global declaration

When variable or other identifiers are declare as global, these identifiers will be in symbol table throughout the execution of the program.

Program example:

int  gMyGlobalVar;	// declare a global variable

void foo(void)

{

int myLocalVar;	// declare a local variable

myLocalVar = 1;	// initialize local variable

gMyGlobalVar = 2; // Set global variable gMyGlobalVar to 2

return;		// When we leave, myLocalVar will be lost

// But, gMyGlobalVar will be alive

}

void main(void)

{

foo( );		// Declare a local variable

return;		// When we leave, gMyGlobalVar will be

//	lost, too

}

#### Local declaration

Unlike Global declaration, variables declared as local will be removed from the symbol table once the routine that declared the variable(s) exits.

Program example:

int  gMyGlobalVar;	// declare a global variable

void foo(void)

{

int myLocalVar;	// declare a local variable

myLocalVar = 1;	// initialize local variable

gMyGlobalVar = 2; // Set global variable gMyGlobalVar to 2

return;		// When we leave, myLocalVar will be lost

// But, gMyGlobalVar will be alive

}

void main(void)

{

foo( );		// Declare a local variable

return;		// When we leave, gMyGlobalVar will be

//	lost, too

}

### Variable Initializations

In Small-C, as soon as variable is declared, it will be initialized to 0. Therefore, programmer does not have to initialize the variables (need to initialize if initialization value is other then 0).

Program example:

void main(void)

{

int  age; 		// declare a variable

age = 17;		// Initialize age to value 17

return;

}

- Identifier (reference): a named memory location

- Variable: an identifier that C / C++ programs use to store values needed by your program.

  - Storage

  - You create them

  - Values can change

  - Naming convention

    - Consists of letters, numerical digits, and the underscore character.

    - Can not start with a digit

    - Can not use a Small-C keywords

    - Should give your variables meaningful names

### Operators

An operator is a symbol that tells the compiler that you want to perform specific mathematical or logical manipulations. Small-C, just like C, has three general classes of operators: arithmetic, relational and logical, and bitwise.

#### Arithmetic Operators

Table 6-1 lists the binary arithmetic operators allowed in Small-C. The operators -, +, *, and / work the same way in Small-C as they do in most other computer languages.

Operator	Action

-		Subtraction, also unary minus

+		Addition

*		Multiplication

/		Division

%		Modular division

Table 6-1	Arithmetic Operators

Integer division truncates any fractional part.

Example:

x = 3 / 2;

Above operation will result in 1.

Modulus operator, ‘%’, produces the remainder.

Example:

x = 5 % 3;

Above operation will result in 2

Modulus operator can only be applied to integers; cannot be applied to floating number.

#### Relation and Logical Operations

In the term relational operator the word relation refers to the relationships that values can have with one another. In the term logical operator the word logical refers to the ways these relationships can be connected together. Because the relational and logical operators often work together, they will be discussed together here. The key to the concepts that underlie relational and logical operators are the ideas true and  false.

The table 6-2 shows the relational and logical operators.

Relational Operators

Operator		Action

>			Greater than

>=			Greater than or equal

<			Less than

<=			Less than or equal

==			Equal

!=			Not equal

Logical operators

Operator		Action

&&			and

||			or

!			not   --- not working yet

~			not   --- nor working yet

Table 6-2	Relational and Logical Operators

#### Bitwise Operators

The term bitwise operation refers to the shifting of the actual bits. Table 12-3 lists the operators that apply to bitwise operators.

Operator		Action

& 			and

|			or

^			exclusive or   --- not working yet

~			not

>>			shift right

<<			shift left

Table 7-3	The Bitwise Operators

#### Assignment statements

The general form of the assignment statement is

variable_name = expression;

where expression may be as simple as a single constant or as complex as a combination of variables, operators and constants. Like C, Small-C uses a single equal sign to indicate assignment. The target, or left part of the assignment, must be a variable and not a constant.

### Precedence and Order of Evaluation

The table below lists the rules for precedence and associatively of all operators that are supported by Small-C.

| Operator | Associativity |
| --- | --- |
| ( ) [ ] | left to right |
| ! ~ ++ -- | right to left |
| * / % | left to right |
| + - | left to right |
| << >> | left to right |
| < <= > >== | left to right |
| == != | left to right |
| & ¦ | left to right |
| ^ | left to right |
| && ¦¦ | left to right |
| = | right to left |

### Expression & Statement

An expression combines variables, constants and operators.

Evaluation of an expression results in a value

Sum = 2 + (3 + num2) * 3;

A statement specifies an action to be carried out by the computer (simple statements must end with a semicolon)

## Program Control Statements

This section discusses the various program control statements. These includes the conditional statements

- if

- switch

, the looping construct

- while

- do-while

- for

, and the statements

- break

- continue

- goto

These statements control the flow of the program.

### IF Statement

#### IF

Syntax:

if (expression)

statement;

Example:

if (age < 5)

put(“Baby”);

if (salary > 40000   || salary < 100000 )

{

printf(“mid class family\n”);

printf(“can not buy home in bay area\n”);

}

#### IF-ELSE

Syntax:

if (expression)

statement;

else

statement

Example:

if (age < 18)

printf(“you are still a kid\n”);

else

printf(“you are on your own\n”);

if (salary < 100000)

{

printf(“you are poor\n”);

printf(“you need to make more\n”);

}

else

{

printf(“ you still might be poor\n”);

printf(“maybe you can buy a run down home\n”);

}

#### Nested IF Statement

Syntax:

if ( condition )

statement

else if (condition)

statement

else

statement

### SWITCH Statement

Syntax:

switch (expression)

{

case constant: statement(s);

case constant: statement(s);

default:	statement(s);

}

Example:

char selection;

selection = 2;

switch (selection)

{

case 0: printf(”Num is ZERO”); break;

case 1: printf(”Num is ONE”); break;

case 2: printf(“Num is TWO”); break;

default:  printf(“Bad data”);

}

### WHILE Statement

Syntax:

while (expression)

Statement

OR

while (expression)

{

Statement(s);

}

### DO-WHILE Statement

Syntax:

do

{

statement(s);

} while(expression)

### FOR Statement

Syntax:

for (exp1; exp2; exp3)

statement;

OR

for (exp1; exp2; exp3)

{

statement(s);

}

exp1 (optional): initialization expression

exp2 (optional): conditional expression (test)

exp3 (optional): loop expression

## Function

Small-C grammar, like standard C/C++, allows function implementation. There are two types of functions:

- Predefined functions

Functions that are predefined by the Virtual machine library.

- User defined functions

Functions that are created by the user (written in Small-C)

Function is equivalent to a subroutine or function in other languages – or procedure. A function provides a convenient way to encapsulate some process (statements) in a black box, which can then be used without worrying about its inner functionality.

### Pre-Defined Function

For the listing of Predefined functions, please refer to Section 7.

### User Defined Function

To write and use user defined function(s), the programmer must do the following

- Declare

- Implement

- Use

- Declare

Syntax:

<return type> <function name>(<parameters>)

- Implementation

Syntax:

<return type><function name> (<parameters>)

{

<code>

return <return type>

}

Example:

int addTwoNum(int, int);		// Declare

void main(void)			// Main function

{

int sum;

sum = addTwoNum(2, 3);		// Use (make a call)

printf(”Sum = %d”, sum);

}

int addTwoNum(int n1, int2)	// Implement

{

int num;

num = n1 + n2;

return num;

}

For more on Function, please refer to C/C++ documentation

## Pre-processor (#include & #define)

### #include

Syntax:		#include “filename”

### #define

Syntax:		#define   MAX_NUM_OF_READS     1000

# WCUBE

## Overview

This application is designed to provide a user interface to CUBE in a Windows environment. Since this tool is designed to manipulate scripts for execution on the drive, it only makes sense to emulate a user interface similar to other integrated compilers such as Visual C++. As a result the application contains a text editor with additional components, specific to CUBE functionality.

## Features

All windows aside from the text editor can be free floating or docked. All windows can be docked on any side to the main window or other docked windows. This allows for the flexibility of user preference in the appearance of the application. Each window, including the main window, remembers its position and visibility when the application is closed. So each time the application is reopened, the same interface will be seen.

Note: Since windows can be docked on any side, there may be difficulties in docking windows in certain positions as they may have a tendency to snap to the undesired edges. Watch the outline of the window when dragging to dock.

The Buffer Editor, Disk Status, and Command History are all free floating while the Command Line is still docked:

Additionally, the windows maybe closed/hidden so there is more room for other windows. There are three ways to toggle the visibility of the various window. You can use the individual close button on the window, use the toggle buttons on the top, or use the file menu.

As you can see, the file menu allows you to hide more windows than the toggle bar. If you really need the space, then they can be closed. However, they are not normally closed since they take minimal space and provide quicker access to various parts of the application. Once a window is hidden, reselect from the toggle bar or the file menu to make it reappear.

All toolbar icons and file menu selections have captions assigned to them. If confused about what a particular command may do, hold the mouse over the item and the status bar will display a more detailed explanation about its function.

Device Configuration

In the menu bar there is an pull down menu for IDE Devices. Similar to the command “setha”, this window allows you to select which device you wish to use.

A list of the devices detected on your system will be displayed. Selecting one of the devices will load the appropriate drivers and register the device for usage on with executable commands. Additionally, there are the options to configure and reduce Windows overhead.

Note: Windows requires an inf installed for each device on the system before you may interact with it. If, in the Device Manager, there is an exclamation point next to a device you wish you use in WCUBE, it will not show up until an inf has been installed and the exclamation point is gone.

The configure option will display a new dialog box which will allow you to hide or show devices on your system.

You will see a similar listing of devices in this window, however each device has a check box next to it. By unchecking the box, the device will not appear in the menu. Additionally, you will be unable to select that device from the command line either. This helps to remove devices you do not wish to test to prevent accidental data loss or damage, such as the OS’s resident hard drive.

Since Windows requires more resources, there is inherent overhead using Windows versus DOS. Checking the “Reduce Windows Overhead” will attempt to minimize this overhead. This will not reduce drive execution time, just the time between each command. Of course, as more system resources are dedicated to WCUBE, other applications may feel more sluggish with this on than without. This option will not affect system performance when no scripts/commands are running.

Note: This option may not work on some systems, particularly Windows 98 machines. If you notice command execution times taking longer than they should with this option, please disable it.

When selecting a device, the name of the window will change. When having multiple WCUBE windows open, you can more easily distinguish which WCUBE belongs to which host adapter. Remember, you can only one WCUBE can select each host adapter.

All of these settings are saved when the application is closed so reselecting and configuring of devices is unnecessary between application restarts.

Text Editor Window/Main Window

### Overview

At the root of the application is the text editor. One could think of the application as a text editor with extra windows. The text editor provides an interface to load and manipulate a script before compilation and execution on the virtual machine. The text editor is very similar to Notepad, but also integrates several other features.

### The Interface

Since the application is the text editor, most of the toolbar buttons and file menu commands only pertain to the text editor. The text editor supports multiple open script files and provides a tab bar for easy navigation between the various each open script. In its maximized state, you can encompass the entire window with a single script file, switching between each file by clicking its tab.  Additionally, there is support for non-maximized viewing, so multiple scripts can be viewed side by side.

At the top there is the file menu and toolbar.

Both provide methods for creating new, opening, and saving files as well as undoing, redoing, cutting, copying and pasting text for each script. Additionally, in the toolbar, there is support for flagging of lines. At the bottom, there is a status bar which provides various information such as the current cursor position, text mode, and key status (num lock, caps lock, etc).

The tabs also provide some repeated functionality. By right clicking on the tab, you can access the same functionality found in the file menu and toolbar for that particular script (right). Right clicking on the bar will produce a different list of options (left).

In addition to basic text entry, the editor supports syntax highlighting, automatic indenting, and flagging/bookmarking of lines.

Syntax highlighting - Most basic C commands are recognized by the editor and will automatically change colors. Such syntax includes: compiler commands (#), quotations (“), numbers (0-9), comments (both // and /**/) and keywords (int, main, char, etc).

Automatic indenting – Like other programming orientated text editors, this editor will automatically indent on a carriage return if the previous line was indented.

Note: the editor will *only* indent if the previous line has been indented (first indent is manually put)

Flagging lines -And finally, one can flag various lines for quick access. This can be done by selecting the flag button in the toolbar or pressing ctrl+<#> where <#> is a number between 0 and 9. This will create a little bubble in the left margin. By selecting “next flag” or “previous flag” in the toolbar, you can jump to the next or previous flag set based upon your current cursor location. If the flag was set by ctrl+<#> you can also press alt+<#> to jump to that specific flag.

The Command Line

### Overview

The command is modeled from the DOS command shell. It allows the user to execute small-c commands directly or execute some limited commands within the application that pertain to script editing.

### The Interface

Like typical shell commands are typed in and feedback regarding the command is reported back.

The above image shows the command line window. At the bottom is the command line itself. This is the main interface to the CUBE compiler and virtual machine. Any commands which are understood by the CUBE compiler can be entered at the prompt.

There are two types of commands, built-in commands, and CUBE commands. Although the built-in commands have very similar, if not exact, counterparts in the DOS CUBE, the underlying structure is different such that they need to be specially written for WCUBE. All commands which do not fall into the built-in commands are assumed to be CUBE commands and automatically compiled.

Built-in Commands:

| Command | Description |
| --- | --- |
| new | The application will open a new, empty script file for editing. No file will be created until explicitly told to save |
| load | The application will open the standard Windows load dialog for you to select a file to open in the text editor |
| load <filename> | The application will attempt to open the file with the specified filename in the text editor |
| loadm <filename> | Load the file as a macro |
| listm | Lists all the macros detected |
| save | The application will save the currently selected text editor window |
| run | The application will run the contents of the currently selected editor window |
| exit | Exit the application. Will prompt to save any scripts that have been modified. |
| cls | Clear all text from the command line |
| * | Whatever cannot be understood will be assumed to be a small-c script and sent to the compiler/virtual machine. Note: the code will be automatically wrapped in “void main() {}” |

Since a press of the enter key will start the execution of a command, the command line only accepts single line commands. For multi-lined commands, use the script editor. Please note for CUBE commands, there is no need to add “void main() {}”, the text will be automatically encapsulated so they can be properly executed.

Like a DOS shell, whenever a command is entered, it is displayed along with any output that may have occurred as a result of the command. Typically an “ok” will display in the window to indicate the completion of the command. Additionally, the prompt along with a blinking cursor will appear so another command may be entered.

The command line also support command history. Any command typed during the current session can be recalled using the down and up arrow keys. The up key will cycle through earlier commands while the down key will cycle through later commands. Once you reach your desired command, you may edit it, or keep as is, for execution again.

While a command is processing, the input will disappear. This will prevent multiple commands being executed on a drive at the same time. Any other part of the application may be used while a command is processing. That is the beauty of Windows and multithreaded applications. To cancel a command, press “ESC” which will attempt to halt any commands currently being executed.

At the top is the CWin (console window). By default it is not shown an the command line encompasses the entire window. It is another place for output to be displayed per the user requests. The display window is attached to the command line window and cannot be detached. Additionally it cannot be resized except through the commands defined by CUBE. The All supported command, including creating and resizing the window, are described in the CUBE documentation.

Buffer Editor

### Overview

The buffer editor is designed to provide a method to view and alter the contents of the disk buffer in its raw format.

### The Interface

This window provides manipulation of a specified buffer. Contained are three tabs to select between buffers, read buffer, write buffer and compare. For each buffer tab, there are three fields provided, from left to right: address field, hex field, and ASCII field. Any field is editable and changes in one will reflect in the others.

The address field will display the range of addresses, in hexadecimal, viewed in the other two fields. Also, the address field provides quick access to a particular address. Just type in the address in hexadecimal and press enter, the buffer will jump to the specified address, if it is valid. Press escape or click to cancel out. While manipulating the data in the other fields, the address field will highlight the address of the data being selected.

The hex field displays the contents of the buffer in hexadecimal and likewise the ASCII field displays it in ASCII. By default the editor is in overwrite mode. Any thing that is typed in will overwrite the existing values. To switch to insert mode, press insert. This will shift all data after cursor to the right and inserting the new value. Additionally, the delete be available, which will shift all data after the cursor to the right

Note: When inserting, the last byte will be “pushed out”. Also, when deleting, the last byte will be shifted in with value 0x00.

At the top, there is toolbar to provide additional functionality other than insert and overwrite. The eight buttons are (left to right) Search, Fill, Commit, Revert/Refresh, Clear, Compare, Copy, and Configure.

Search button – displays a dialog enter either a hex or an ASCII value. This value will be searched for within the entire buffer.

Fill button – display a similar dialog as the search button. This will to fill the entire buffer with the specified pattern.

Note: When entering hex, the input must be byte aligned, that is, your searches must be multiples of 8 bits wide (i.e. “000A” and “0A” is ok, but “00A” or “A” is not).

Commit button – copies all modifications to the actual buffer. No actual modifications are made to the buffer until the commit button is pushed.

Revert/Refresh button – undoes any changes since last commit and reload the current buffer values into the window. This is useful if any undesirable modifications were made. Also this button can be used to get the current state of the buffer.

Clear – This will clear the buffer of all values, replacing everything with zeros. At the bottom, the status bar displays, from left to right, the mode (insert or overwrite) and the cursor position in both decimal and hexadecimal values.

Compare – This toggles the compare between read and write buffers, highlighting the differences in the buffer you are currently in.

Copy – This will pop up a new window to copy various selections from one destination to the other. The copy range will automatically be filled with the whatever you are selecting.

Warning: Copying large amounts of data from the buffer is not recommended as the process is slow. If you need to dump the entire read/write buffer, use rdump/ wdump, or rsave/wsave commands.

Configure – This will open a window to allow you to customize the appearance of the buffer. The scrollbar range is for making the scroll bar not scroll for the entire buffer. This is useful when you only want to look at 10 blocks of data, and you don’t need the scroll bar to be sensitive for the entire 4000 blocks.

Command History

This is only a window to provide diagnostic information. The window is non editable and displays a history of the command executed on the drive. The contents of the window update automatically.

Disk Status

Similar to the command history, this window is used to provide diagnostic information about the drive. There is interface to the user other than what is displayed.

The window shows what the internal c, h, s, and l are set at. Additionally the # of reads/writes/seeks and corresponding soft and hard errors are reported.

Disk Info

This window displays information gathered about the drive. It will update whenever the command “id 1” or “config” is issued. These commands gather information from the drive. The window will remember the last “id 1” command issued as well as the last “config” command issued. The output will be the output from “id 1” followed by the output from “config”. If either of these commands have not been issued, their respective areas in the window will remain blank.  Click on each tab to switch between each view.

Flags

This window shows the built in flags in WCUBE. The names are similar to what you would type in at the command line. If the flag is enabled, there will be a check by it, otherwise it will be unchecked. The flag will update in “real-time”; whenever the a flag changes, in a script, command line or mouse click, it will be reflected immediately.  All flags can be modified at anytime, even while a script is running with the exception of logfile. To turn on and off the logfile, you must type it in at the commandline or within a script.

Macros

This window lists all the macros in a file whenever a macro file is loaded either through the file menu or “loadm”. This is the same list displayed at load time or when the “listm” command is issued. To run any of the macros, double click on it and the macro will run, as if you had typed “run <macro name>”

Notes on Compatibility Mode

NOTE: We are not responsible for any data lost if you accidentally write over your OS drive. If you are using Windows 98, proceed with caution as it is not as stringent as Windows 2000/XP to protect the OS drive. If at any time you receive a message that you must reboot, most likely you have selected an invalid choice. Undo you selection or you risk no longer being able to boot to the drive. Although not recommended, you can run can use the primary port for the OS drive and secondary port for the test drive (or the other way around).

If you are using second channel on the board, if you find you are unable to talk to the drive or a [?] appears instead of [0] in the title bar of WCUBE you need to type DRIVE = 1 (defaulted to DRIVE = 0) then try selecting the host adapter again. This will cause WCUBE to use the second port rather than the first. WCUBE does not remember what port you are using from session to session. It will always default to DRIVE = 0. To remedy this, write a cube.ini which sets DRIVE = 1 then setha <host adapter number>.

Now for installation. You do not need to install the WCUBE drivers to use the motherboard controllers. Instead you need to disable the device in device manager. Go to your Device Manager and find the channel you wish you use:

Right click on the channel and click Disable. Windows may or may not give you a warning message that this will make the device no longer function. Click yes and the device should appear with a red ‘X’ now. You can now use compatibility/onboard in WCUBE.

Known Issues and Notes

Marvell Bridge Chip:

There is a known bug regarding SATA drives that use the Marvell bridge chip. When executing physical commands, sometimes the drive fails to raise an interrupt at the proper times. As a result, we have implemented a polling mechanism as a work around for this issue. The drivers will poll once every millisecond when a physical command is issued, up to the user defined timeout.

This works in conjunction with the standard interrupt method, and acts as a failsafe if no interrupt is seen even though the drive is ready/waiting for the host to take action.

It should be noted that, for drives that affected by this, each “lost” interrupt (usually one interrupt per block transferred) can add up to ten milliseconds to the overall command time. The command time reported by WCUBE, under these circumstances, is not reliable.

To disable the DRQ polling, and rely only on interrupts, disable the flag “drqpolling” (drqpolling 0).

- The CUBE

The CUBE is drive test software which allows the users to interactively test and FA drives.

Some of its key features are:

- Small-C script language

- ATA-7 Command Set (Both Extended & Non-extended commands)

- Support DMA and UDMA

- Support Power Controller Board:

  - Supports Samsung ISA Power Control board

  - Support Parallel Power control using the ATX power supply

- Advanced Write/Read buffer management

- Feature to trace (command history) – currently, it is configure to trace upto 100 last commands executed (command block / error status / execution time)

- Advanced Execute Timer Clock (execution time clock in microseconds)

- Provides Consol Control commands (user can define and display data on a user defined console window)

- Many other features are available

## CUBE.INI file

Cube, when loaded, will first look for CUBE.INI. This is CUBE initialization file which Cube will execute. If the file does not exist, cube will still load but no initialization will take place. Meaning, the user must set things up manually before drive can be tested.

CUBE.INI file content syntax follows Small-C grammar. The kinds of thing one would do inside the CUBE.INI will be such a setting as setting up the power controller type, PATA or SATA controller to load. Below is a sample CUBE.INI for your reference:

//-------------------------------------------

//- By:         Daniel

//- Date:       08/08/2003

//-

//- This is the CUBE Initialization file

//-

//- Here, we will scan for controller and

//- set/load driver for the first controller found

//-------------------------------------------

void main(void)

{

scanallpci;

setha(0);

PWR_CONTROL=1;

return;

}

## Macro support

Macro is a prewritten set of instruction that can be called from command line. To utilize this feature, the user must first put together a macro file, load macro file, then call the macro he/she wants to run. There are two commands that must be used when loading and calling of a macro:

- loadm <macro filename>

  - ex: loadm mymacro.mac		// file extension can be anything

- to run, type in macro name from the command line

  - ex:   seektest

Macros will not take in any call parameters. All parameter, argument, passing must be done using the predefined global variables (ex: R0-R19). Also, macros must not return any return types. Therefore, all macro definitions must follow the following syntax:

Syntax:		void	<macroname>	  (void)

Example”		void   test1 (void)

{

statement(s);

return;

}

example of macro file:

//-------------------------------------------

//- By:         Daniel

//- Date:       07/19/2004

//- FileName    MyMacro.MAC

//-

//- Macro file demonstration

//-

//-------------------------------------------

void mytest(void)

{

id 0;

sk( 1,1);

rdmae(1,1);

}

void msg1(void)

{

put(“This is message”); newline;

put(“This is a message”);

}

Above simple example has two macros define, mytest & msg1.

To use these macros, one CUBE is lunch, you’ll do the following:

- loadm mymacro.mac		// load macro file

- msg1				// run’s macro “msg1”

- mytest				// run’s macro “mytest”

## CUBE Built-in/Predefined Functions and Variables

- Command line commands

- Basic IO functions

- Console display functions

- PCI functions

- Drive command functions

- Buffer functions

- Control Flag Switches

### Predefined Variables

These variables are predefined and can be accessed by script files.

| Identifier | Description |
| --- | --- |
| R0 – R19 | Reserved Variable for the users |
| VU | Vendor Unique mode flag (0 == no, 1 == yes) |
| DRIVE | Drive selector (0 == Primary, 1 == secondary) |
| SLAVE | Drive selector (0 == Master, 1 == slave) |
| ECC | ECC byte count (set when Identify command is issued) |
| RETRY | Retry count |
| DEVICE_TYPE | DUT device type (set when Identify command is issued) 0 == Unknown 1 == PATA 2 == SATA 4 == SDIO |
| CMD_TIMEOUT | Command Timeout value in milliseconds. The default is 10,000. The value can be modified using cmdtimeout(exp) function. ex: cmdtimeout(123); // timeout value changed to 123milliseconds |
| acc | Accumulator (was added to support Gemini like parameter passing on some VU commands) |
| MAX_C | Max cylinder (set when Identify command is issued) |
| MAX_H | Max head (set when Identify command is issued) |
| MAX_S | Max sector (set when Identify command is issued) |
| MAX_LBA | Max lba (set when Identify command is issued) |
| MAX_Z | Max zone (set when “init” command is issued to drive) |
| MAX_PC | Max Physical Cylinder (set when “init” or “inith” is issued to the drive) |
| MAX_PH | Max Physical Head (set when “init” or “inith” is issued to the drive) |
| MAX_PS | Max Physical Sector (set when “init” or “inith” is issued to the drive) |
| MAX_PBA | Max Physical Block Address (set when “init” or “inith” is issued to the drive) |
| MIN_PC | Minimum Physical Cylinder accessible (set when “init” or “inith” is issued). Any VU command accessing below this cylinder will be rejected. |
| c | Current cylinder addressed (automatically picked up by VU commands, if used) |
| h | Current head addressed (automatically picked up by VU commands, if used) |
| s | Current sector addressed (automatically picked up by VU commands, if used) |
| l | Current lba addressed |
| TF_ERROR | Last error register read (updated when drive cmd is issued or on “rtsk” |
| TF_STATUS TF_SC TF_SN | Last status register read (updated when drive cmd is issued or on “rtsk” Updated when “rtsk” cmd is issued (current register only) Updated when “rtsk” cmd is issued (current register only) |
| RBUF | Read buffer assigned |
| WBUF | Write buffer assigned |
| PCI_BASE | PCU base address selected (set when setha(HA#) is issued) |
| CMD_TIME | Last command execution time (set when cmdtime 1 is issued) |
| PWR_CONTROL | Power controller type specifier (default is set to 1) 0 == No power controller 1 == Parallel control 2 == Samsung ISA power controller 3 == 4 == Samsung PCI power controller |
| TREAD | Total read count |
| SREAD | Total read soft error count |
| HEREAD | Total Hard error count |
| TWRITE | Total write |
| SWRITE | Total write soft error |
| HEWRITE | Total write hard error |
| TSEEK | Total seek |
| SSEEK | Total seek soft error |
| HESEEK | Total seek hard error |
| ERRORHALT | To Halt the test on user input error (Error register) erhlt must be set to 1 |
| NOTDONE | Used for ADDH, ADDC, when max cylinder is reached for all heads this variable is cleared to zero. |

### Command-line Commands

These commands are valid only when used from the console prompt. These commands are not part of the Small-C language. Therefore, user can not include these commands inside the Small-C program.

| function syntax | parameter / description | requirement |
| --- | --- | --- |
| cls | Clear console window content | NA |
| load <filename> | filename: name of the file to load | NA |
| loadm <macro filename> | Macro filename: name of the file to load |  |
| run or r | Run script | Script must be loaded using the “load” cmd |
| run <mac func> or r <mac func> | Run macro function | Macro file must have been loaded and the macro must exist |
| edit <filename> | Edits a file: If filename exists it loads the file to be edited. If not opens a new file | load editor and edit currently loaded script. If no file loaded, open an empty file |
| exit | terminate CUBE |  |

### Console: Function Keys

| Key | Description |
| --- | --- |
| F1 | Toggle Status window |
| F2 | Toggle Console screen mode (size: 25 lines vs 40 lines) |
| F3 | Show command execution trace buffer (this assumes “trace 1” was issued before) |
| F4 |  |
| F5 |  |
| F6 |  |
| F7 |  |
| F8 |  |
| F9 | Show symbol table |
| F10 |  |
| ESC | Stop script execution |

### Edit

This is a very simple edit that work a barebones of an editor.  If large file is used, it is recommended to use editor outside of Cube.

To use the editor type      edit  <filename>  .

If filename exist, it will load the file, if not, it will open a file with <filename>.

F1    : Help

F3    : Search                      
F4    : RepeatSearch                
F5    : Save                        
F6    : Mark Block                  
F7    : New File Save               
Ctrl-X: Delete line, or delete Block
Ctrl-V: Paste line, or Paste Block  
ESC: quit the editor and bring you back to the command prompt

These are the keys that works in this editor.

Control_X , Control_V, Insert, Delete, Home, PageUp, PageDown, Backspace, UpArrow, Down Arrow, Left Arrow, and Right Arrow.  Of course and all the letters and numbers works also.

Figure 1 Cube editor

At the top of the editor screen , it shows the file name “c”, and the bottom right corner shows the current insert key mode.

At the top Right corner shows the current line number.

F1: is the help  key

F6: is the mark block function.

To mark, first press F6 and then move your cursor up or down to mark the block and then control _x to cut and control_v to paste

Figure 2 Cube Editor Help

### Help

Help is for those who needs instant help without going to the cube.doc.  The contents of  the help file is same as the cube.doc.

On the console:

‘?’ will print help on help.

‘??’ will invoke the help screen where the help file will be displayed.

Figure 3 cube help

‘?partial word’ will find string matches the beginning of the partial word.

Example:

?wr

wr(a, h,s,b)

wre(a,b)

wrle(l,s1,s2)

wrtc current

wrxr val

wrxw val

wrbf  val

so if you want to find out more about a command get closer to the command as you can

example:

?wr(

wr(a, h,s,b)

0x30 Write Sector - PIO

a: Cylinder or LBA

h: head - valid only in CHS mode

s: sector - valid only in CHS mode

b: #of blocks to read

### Console: Basic I/O Functions

Theses commands are used display data unto Cube console window.

| function syntax | parameter / description | requirement |
| --- | --- | --- |
| put(str) | Display string to console window | NA |
| putd(fmtStr, int) | Display formatted string with integer number to console window | NA |
| putf(fmtStr,float) | Display formatted string with float number to console window | NA |
| puts(fmtStr,str) | Display a fmtStr string with str to console window | NA |
| printf(…) | A format specification, which consists of optional and required fields, has the following form: %[flags] [width] [.precision] [{h ¦ l ¦ I ¦ I32 ¦ I64}]type Each field of the format specification is a single character or a number signifying a particular format option. The simplest format specification contains only the percent sign and a type character (for example, %s). If a percent sign is followed by a character that has no meaning as a format field, the character is copied to stdout. For example, to print a percent-sign character, use %%. The optional fields, which appear before the type character, control other aspects of the formatting, as follows: type Required character that determines whether the associated argument is interpreted as a character, a string, or a number. c,x,d,s,f flags Optional character or characters that control justification of output and printing of signs, blanks, decimal points, and octal and hexadecimal prefixes. More than one flag can appear in a format specification. -,+,0,’ ‘,# width Optional number that specifies the minimum number of characters output. precision Optional number that specifies the maximum number of characters printed for all or part of the output field, or the minimum number of digits printed for integer values. h ¦ l ¦ I ¦ I32 ¦ I64 Optional prefixes to type-that specify the size of argument. | NA |
| newline | Put new-line character to console |  |
| getchar(var) | Get a byte from the user and store it into var | NA |
| getd(prompt, var) | Get a integer from the user into var prompt: a string to display var: variable to place data example: getd(“Give me data: “, R0); |  |
| getf(prompt, var) | Get a float number from the user and store it into var |  |
| gets(prompt, var) | Get a string from the user and store it into var | Not Supported At This Time |

### Console: Display Functions

Theses commands are used for controlling/displaying formatted text unto user defined display. For any of the following functions to work, one must issue cwin( ) function first.

| function syntax | parameter description | requirement |
| --- | --- | --- |
| cwin(size) | Create user console window | NA |
| gotoxy(x,y) | Place user console cursor at x,y | cwin |
| getxy(x,y) | Get x,y coordinate where the cursor is | cwin |
| cputs(x,y,str,attr) | Place a text at x,y on user defined window with attribute attr | cwin |
| cputd(x,y,fmtStr,n,attr) | Place a text and integer at x,y on user defined window with attribute attr | cwin |
| cputf(x,y,fmtStr,n,attr) | Place a text and float number at x,y on user defined window with attribute attr | cwin |
| ccls | Clear user define window | cwin |

Color Attributes:

| Value | Background | Foreground |
| --- | --- | --- |
| 0 | Black | Black |
| 1 | Blue | Blue |
| 2 | Green | Green |
| 3 | Cyan | Cyan |
| 4 | Red | Red |
| 5 | Magenta | Magenta |
| 6 | Brown | Brown |
| 7 | White | White |
| 8 | Blinking Black | Dark gray |
| 9 | Blinking Blue | Light blue |
| A | Blinking Green | Light green |
| B | Blinking Cyan | Light cyan |
| C | Blinking Red | Light red |
| D | Blinking Magenta | Light magenta |
| E | Blinking Brown | Yellow |
| F | Blinking White | Bright white |

ex:

void main(void)

{

cwin(5);		// create a user console window of size 5 (max of 5 lines)

cputs(1,1,”Hello!”, 0x35);	// Display “Hello” at xy coordinate with attribute of 0x35)

return;

}

### Run-time Control Flag Switch

Following function calls turn run-time flag switches ON or OFF

| function syntax | parameter description | requirement |
| --- | --- | --- |
| logfile <0/1> | Turn logfile logging feature on or off (log data is saved to CUBE.LOG) – User defined console outputs are not put into log file. 0 – Turn it off 1 – Turn it on |  |
| dtsk <0/1> | Turn on/off TF echoing (TF will be echoed before TF is sent to the drive) 0 – Turn it off 1 – Turn it on |  |
| tag <0/1> | Turn on/off write buffer data tagging 0 – Turn it off 1 – Turn it on |  |
| trace <0/1> | Turn on command tracing (upto 100 last cmds will be captured) 0 – Turn it off 1 – Turn it on |  |
| erhlt | Turn on/off stop on error feature (when drive error is encountered, or buffer miscompare, the script will halt) 0 – Turn it off 1 – Turn it on |  |
| slba | Turn on/off LBA addressing (used with drive commands) 0 – Turn it off 1 – Turn it on |  |
| bcmp | Turn on/off buffer comparing (works with drive data read commands) – if the feature is on, and miscompare occurs, cube will show the miscompare data 0 – Turn it off 1 – Turn it on |  |
| cmdtime | Measure command time and store the data to CMD_TIME global variable (user can access this variable to obtain the command execution time in microseconds) 0 – Turn it off 1 – Turn it on |  |
| verbose | Turn on/off verbose mode (system messages) 0 – Turn it off 1 – Turn it on |  |
| updatestat | Turn on/off visual updating of status of disk (c/h/s/l, errors). Can improve performance but no visual indication that script is running. 0 – turn off updating 1 – turn on updating |  |
| updateec | Turn on/off updating EC When there is a error, 1: will set the Global variable EC 0: will not set Global variable EC |  |
| drqpolling | Turn on/off polling of DRQ on data transfers. Used incase of missed interrupts 0 – turn off polling 1 – turn on polling |  |
| exit | Exits the cube |  |

ex:

void main(void)

{

cmdtime 1;	// Turn on command time measurement

sk(1,1);		// seek to cyl=1, head=1

putd(”CMD EXCUTION TIME: %d”, CMD_TIME);

return;

}

When “erhlt 1” is issued and we get an error, the system will halt with option of either to STOP or to CONTINUE. If Continue is selected, Cube will read and dump TF contents and dump the trace buffer – if tracing is enabled.

### Trace/Debug functions

| function syntax | parameter description | requirement |
| --- | --- | --- |
| trace <0/1> | 0 - turn off command tracing 1 – turn on command tracing |  |
| trace_show(n) | show n number of traced data (the last n). If n==0, show all captured traced data. | “trace 1” must be issued before hand |
| trace_clear | clear trace buffer |  |
| trace_lastcmd(var) | store last command issued into var | “trace 1” must be issued before hand |
| debug <0/1> | 0 - turn debugging off 1 – turn debugging on | This option should be used only by CUBE developers |

From the console window, you can also use F3 key to displace trace buffer

ex:

void main(void)

{

trace 1;		// Enable tracing

id(1);		// Issue identify command

sk(1,1);		// Seek to cyl=1, head=1

trace_show(10);	// Display upto 10 last cmds issued

return;

}

When “erhlt 1” is issued and we get an error, the system will halt with option of either to STOP or to CONTINUE. If Continue is selected, Cube will read and dump TF contents and dump the trace buffer – if tracing is enabled.

### Buffer functions

In Cube, there are 2 predefined buffer.

ex: buf1, buf2.

The user can map read/write buffer to one of the predefined buffer.

ex:

setrbuf(1);		// sets read buffer to buf1

setwbuf(2);		// sets write buffer to buf2

By default, when Cube is loaded, read buffer is set to buf1 and write buffer is set to buf2

Example:

To tag and fill write buffer:

tag 1;

wfill(0xffffffff);

| function syntax | parameter description | requirement |
| --- | --- | --- |
| atoi(str1,offset,radix,rtnval); | Changes str into a number Changes str1 from offset to change to a number using radix as the base. |  |
| strcmp(str1,str2,len,rtnval); | Compares str1 to str2 of length len Rtnval=0 if equal Rtnval non zero otherwise |  |
| strcat(str1,str2); | Concats str2 to end of str1 |  |
| strcpy(str1, str2); | Copies str2 to str 1 |  |
| setrbuf(exp) | set read buffer to predefined buffer id “exp” exp can be 1 or 2 (there are 2 predefined buffers) |  |
| strlen(str1,rtnval) | Puts strlen(str1) into returnval |  |
| setwbuf(exp) | set write buffer to predefined buffer id “exp” exp can be 1 or 2 (there are 2 predefined buffers) |  |
| wfill(pattern) | Fill write buffer with data pattern | Pattern must be in the hex format |
| rfill(pattern) | Fill read buffer with data pattern | Pattern must be in the hex format |
| wfillb(string, num) | Fills the buffer with the string pattern, containing num of bytes Example: wfillb(“aabbccddeeff1100”,8) |  |
| wdump(start, count) | Dump write buffer content from offset start for count number of bytes |  |
| rdump(start, count) | Dump read buffer content from offset start for count number of bytes |  |
| bdump(start, count) | Dump write & read buffer content from offset start for count number of bytes (side-by-side) |  |
| Bswap | Swap write buffer and read buffer (read buffer becomes write buffer and visa-versa) |  |
| rpeekb(var, offset) | Get a byte from the read buffer at offset offset |  |
| rpeekw(var, offset) | Get a word from the read buffer at offset offset |  |
| wfillsp(pat) | pat: 1: Incremental 01020304…. 2: Address pattern FFEEDDCC 3: ID pattern using c/h/s/b writes in in BCD,hex, and inverse of c/h/s/b 4: IQ pattern fills in sector with the current LBA and subsequently increments the value. 5: Random pattern |  |
| wpeekb(var,offset) | Get a byte from the write buffer at offset offset |  |
| wpeekw(var,offset) | Get a word from the write buffer at offset offset |  |
| rpokeb(offset, var) | Put a byte into read buffer at offset offset |  |
| rpokew(offset, var) | Put a word into read buffer at offset offset |  |
| wpokeb(offset, var) | Put a byte into write buffer at offset offset |  |
| writeb(offset,data) | Puts data string into the write buffer Example: writeb(0,”aabbccddeeff11002233”); |  |
| wpokew(offset, var) | Put a word into write buffer at offset offset |  |
| bedit bufferId | Edit the buffer referred to by buffer ID. Buffer ID =1 for read buffer, or 2 for write buffer |  |
| brload filename | Loads the read buffer with entire contents of file referred to by filename or 0x400000 bytes which ever is less. | File must exist |
| bwload filename | Loads the write buffer with entire contents of file referred to by filename or 0x400000 bytes which ever is less. | File must exist |
| brsave filename | Saves read buffer content to the file with filename. Whole 0x400000 bytes are saved. |  |
| bwsave filename | Saves write buffer content to the file with filename. Whole 0x400000 bytes are saved. |  |
| bsave ( BufID, FileName, from, to) | Saves buffer content to the file with filename. BufID 1=read, 2=Write FileName : name of the file to save to From: offset To: length Example: bsave(1,”save.bin”,0,512); |  |
| brloadtrace | Loads the trace command buffer into the read buffer |  |
| bw2r(count) | Copy write buffer to read buffer Count : sector count |  |
| br2w(count) | Copy read buffer to write buffer Count : sector count |  |
| bcopy(desBufId, desOffset, srcBufId, SrcOffset, count) | Buffer copy from srcBufId to desBufId desBufId : buffer # 1 ~ 3 SrcBufId : buffer # 1 ~ 3 desOffset : byte offset from the beginning srcOffset : byte offset from the beginning count : byte count # to copy |  |
| fopen(filename,mode) | Filename: name of the file to open Mode: 1=binary, 0 for text |  |
| fclose(); | Close the opened file |  |
| ftell(rtnval); | Rtnval: returns the current file position |  |
| fseek(pos); | Sets the file pointer to pos Pos: file pointer position |  |
| fwrite(BufNum,offset,len); | Writes the length of buffer from the offset BufNum:Buffer Number, 1,2,3 Offset: offset of the buffer to write Len: length of the data to write |  |
| fread(BufNum,offset,len); | reads the file into the buffer starting offset of the buffer with the length of len BufNum:Buffer Number, 1,2,3 Offset: offset of the buffer to read in Len: length of the data to read |  |

### Bedit

When the user type Bedit with parameter ‘1’ or ‘2’, a buffer editor will popup.

Buffer size is limited to 8192 blocks = 4194304 bytes.

Figure 4 Buffer Editor

1. Shows the offset of the data at the cursor, value is the current data value of where the cursor is.(see Figure 4 Buffer Editor)

2.  Shows the data as ascii format.(See Figure 4 Buffer Editor)

3.  This is the menu for the buffer editor. (See Figure 4 Buffer Editor)

F1: will toggle the cursor between ASCII area anf HEX area

F2: Put the cursor at a data and press F2 will fill that line with the same data as where the  cursor is. (See Figure 5 Fill Line  :F2)

F3. Search the buffer the data

F4.  Swaps buffer between Write Buffer, and Read Buffer

F5. Saves the buffer

F6. Sets all the data back to zero

F7. Compares Data between Write Buffer and Read buffer.  The mis compared data will be in purple(See Figure 7 Comparing the buffer F7).

F8. Clears the buffer

F9. Put the cursor at a data and press F9 will fill the whole buffer with the same data as where the  cursor is.  (See Figure 6 Fill Whole Buffer :F3)

ESC: Quits the buffer and go back to the cube command prompt

PgDn: Goes to next 512 bytes of data when full screen.  If pass  the limit, it will go back to offset zero.

PgUp: Goes to previous 512 bytes of data when full screen. If  pass zero, it will go the 1ff00.

Home: Goes to the beginning of the offset for that screen.

End : Goes to the end of the offset for that screen .

Insert key: Toggles insert/overwrite.

Figure 5 Fill Line  :F2

Figure 6 Fill Whole Buffer :F3

Figure 7 Comparing the buffer F7

### Power Control Functions

User can attach a power control board to a test system to turn power on or off.

| function syntax | parameter description | requirement |
| --- | --- | --- |
| PWR_CONTROL | this is a predefined variable for defining the type of power controller is installed. The definitions are as follows: 0 == No power controller 1 == Parallel control (using ATX power supply) 2 == Samsung ISA power card |  |
| power 1/0 | Turn on/off power 0 – Turn it off 1 – Turn it on | PWR_CONTROL must be set to appropriate controller value. If PWR_CONTROL setting is set to 0 (no power controller), then the program will prompt the user to either turn power on manually or off when power command is received |
| powermargin (switch, 5V, 12V, port, comport) | Switch Turn on/off power 0 – Turn it off 1-- Turn it on 5V: value for 5V, in 100’s example: for 5.25V ->525 12V:value for 12V, in 100’s example: for 12.75 V ->1275 port – port number of serial 8 port power card—0, if N/A comport – comport of the powercard 0, if N/A | PWR_CONTROL must be set to appropriate controller value. For Flexstar power, margining. Power can be turned off either by using “powermargin(0,0,0,0,0)” or “power 0” |
| powr 1/0 | Turn on/off power 0 – Turn it off 1-- Turn it on Waits for start up time. Displays the time to ready in seconds | PWR_CONTROL must be set to appropriate controller value If PWR_CONTROL setting is set to 0 (no power controller), then the program will prompt the user to either turn power on manually or off when power command is received |
| ispower(port,rtnval) | Sets the rtnval to 1 if the drive exist in the power port | FOR PWR_CONTROL TYPE 5 |
| spower(chkrdy,onoff,port,comport) | Turns power on and off Chkrdy: 1: wait for drive ready Onoff: turn on or off Port: power port 1-8 Comport: comport to control power card | PWR_CONTROLTYPE=5 |

#### ATX Power Control Via Parallel Port (PWR_CONTROL = 1)

Figure 8 ATX power Control card

### PCI functions

Before CUBE can communicate with the drive under test, the user must detect and load appropriate driver (PATA/SATA). This can be done by using PCI functions

| function syntax | parameter description | requirement |
| --- | --- | --- |
| scanpci | Scan the PCI bus for predefined SATA/PATA controller (If found, it will display the controller with HA#) |  |
| scanallpci | Scan the PCI bus for any controller (all found devices will have HA# assigned) |  |
| setha(HA#) | Sets and load device driver for the HA# |  |
| pciread(var, offset) | When setha(HA#) is issued and appropriate driver is loaded, the predefined variable PCI_BASE will be set. This command will allow the user to access the register at offset – read in dword data from offset into var | Must first identify the controller by issuing scanpci or scanallpci. Then, Load appropriate driver by issuing setha(HA#) |
| pciwrite(dword, offset) | Write dword data to pci register at offset offset |  |

### Memory Mapped IO

If you are working with a new hardware where writing and reading of data to the HW is done via the memory mapped IO, you must use the following predefined functions to operate on it.

Memory mapped IO operations are done in conjunction with PCI function (see PCI functions section for more info)

| function syntax | parameter description | requirement |
| --- | --- | --- |
| map_phys(mapped_addr, phys_addr, size) | map physical (HW) memory io space into software accessable memory space. mapped_addr: mapped address (returned value from the function) phys_addr: physical memory space to map size: amount of data bytes to map (must be in blocks of 0x1000 bytes) | Caller should have used pciread() function to obtain the physical address to map prior to calling this function. |
| free_phys(mapped_addr) | Free mapped memory. This function must be called at the end of your program to free up the memory space. mapped_addr: address to free | assumes memory was already mapped before freeing |
| gmem32(var, mapped_addr) | Read DWORD worth of data from mapped address into var. var: returned data mapped_addr: memory location to read from | memory was mapped – map_phys(…) |
| smem32(data, mapped_addr) | Write DWORD worth of data to mapped address space. data: DWORD data to write mapped_addr: memory location to write to | memory was mapped – map_phys(…) |

*** It is important to note that when mapping a physical memory space, it must be mapped in blocks of 0x1000.  ie. you must mask the hardware address with 0xFFFFF000 prior to calling the map_phys(..) function.

ex: if your HW memory address is 0x1FC13204, and want to read offset 0x10 from it, you must do the following:

hw_addr = 0x1FC13204;

hw_addr = hw_addr & 0xFFFFFFF0;	// must always mask of last 4 bits

new_hw_addr = hw_addr & 0xfffff000;

difference  = hw_addr – new_hw_addr;

map_phys(mappedAddr, new_hw_addr, 0x8000);  // map memory

new_mappedAddr = mappedAddr + difference;	// compute new addr

gmem32(data, new_mappedAddr + 0x10);		// get data

free_phys(mappedAddr);				// free up memory space

Running code example (Reading & Writing using memory mapped io scheme on Si3124 controller):

//==========================================================

//= By: Daniel

//=

//= Memory mapped io example using CUBE

//=

//=    - we will flash the LED of Si3124 card (Silicon Image SATA-II card)

//=

//==========================================================

void main()

{

int BAR1;                    // PCI config space BAR1 register

int mappedAddress;           // Will hold mapped io space addr

int difference;

int offset;

put("BAR1 - LRAM dump");newline;

pciread(BAR1, 0x18);		// Read BAR1 (PCI Configuration Space)

R0 = BAR1 & 0xFFFFF000;

difference = BAR1 & 0x00000FF0;

map_phys(mappedAddress, R0, 0x8000);

R0 = mappedAddress + difference;

newline;

putd(" mapped io address: R0 = %X", R0); newline;newline;

offset = 0;

for (R10=0; R10 < 20; R10++)

{

smem32(0x8000, R0+0x1000);      // LED on

delaym(50);

smem32(0x8000, R0+0x1004);      // LED off

delaym(50);

}

free_phys(mappedAddress);

}

### Other & Date/ Time

| function syntax | parameter description | requirement |
| --- | --- | --- |
| randomize | NA | NA |
| rand(var, minV, maxV) | var: place to store random number minV: lower limit maxV: upper limit | NA |
| timestamp(str1) | Sets str1 with the current time (hh/mm/ss) |  |
| time | display current time (hh/mm/ss) | NA |
| gettime(var) | get system elapsed time (elapsed since Jan. 1, 1970) in seconds. example: void main() { int sTime; int eTime; gettime(sTime); delays(10); // delay for 10 seconds gettime(eTime); putd(”Diff: %d”, eTime-sTime; } |  |
| datestamp(str1) | Sets str1 with the current date (mm/dd/yy) |  |
| date | display current date (mm/dd/yy) | NA |
| delays(sec) | delay sec seconds |  |
| delaym(msec) | delay msec milliseconds |  |
| clock | display current time in milliseconds |  |
| cmdtimeout(msec) | Set drive command timeout value to msec Default is 10,000 milliseconds |  |
| starttimer | Save current clock into global variable “TICK”. This is a prerequisite for “ts“ command. |  |
| stoptimer | Get and show the elapsed time since previous “st” command. |  |

### Legacy Command Tag-Queue

| function syntax | parameter description | requirement |
| --- | --- | --- |
| showq | Show outstanding queue cmds that has yet to be serviced – cmd issued but waiting to be serviced |  |
| checkq | check DUT to see whether it has any cmds to service. If so, service it. |  |
| debug_cmdq <0/1> | enable/disable debug verbose mode (for cmdq) 0 – Disable 1 – Enable |  |
| rdmaqe(lba, b, tagId) | issue extended read cmdq with tagId. Cmd will be serviced when checkq cmd from script is issued |  |
| wdmaqe(lba,b,tagId) |  |  |
| rdmaq(lba,b,tagId) |  |  |
| wdmaq(lba,b,tagId) |  |  |

example:

//=================================================

//= By: Daniel

//=

//=     Tag Cmd Queue example using CUBE

//=

//=================================================

void main(void)

{

int tagId, lba;

id(0);                   // Device identify

trace 1;                 // Turn on TRACE (for debugging)

cmdtime 1;               // Enable cmd time measurement

//    (to see execution time)

for (tagId=1; tagId<10; )    // for tag ID 1 to 30

{

rand(R0, 0, MAX_LBA); // Obtain random LBA

rdmaq(R0,1,tagId);    // Issue ReadCmdQ

tagId++;

}

for (R0=10; R0; R0--)

{

delaym(500);          // Wait for 500 milliseconds

checkq;               // Check to see whether we have any

//   outstanding cmdq that needs

//   servicing. If so, checkq will

//   service it

}

showq;  // see if anything is left in the Q

// If so, it means not all command was serviced

return;

}

### Native Command Queuing

In order to use Serial ATA Native Command Queuing commands over a particular Serial ATA port, three requirements must be met:

- The host controller NCQ feature (must support the DMA Setup FIS and the Set Device Bits FIS in order to enable First Party DMA transfers and efficient command completion)

- The software driver must support the Read FPDMA Queued and Write FPDMA Queued commands.

- The drive must support Serial ATA Native Command Queuing.

| function syntax | parameter description | requirement |
| --- | --- | --- |
| gettagid(var) | var: tag id available |  |
| rfpdma(lba, nb, tagId) | Read First Party DMA tagId: cmd tag id lba: lba location to read nb: num of blocks to read | SATA drive supporting Native command queueing. Must provide valid tagId – user should make a call to gettagid(var) to request for an available tag id |
| wfpdma(lba, nb, tagId) | Write First Party DMA tagId: cmd tag id lba: lba location to read nb: num of blocks to read | SATA drive supporting Native command queueing. Must provide valid tagId – user should make a call to tagid(var) to request for an available tag id |
| scontrol(var, dir) | dir: direction bit (0 == read, else write) var: if dir==0, var will have scontrol read value. Else, var is the data to be written to SCONTROL register |  |
| sstatus(var) | var: data read from SSTATUS register |  |
| serror(var, dir) | dir: direction bit (0 == read, else write) var: if dir==0, var will have serror read value. Else, var is the data to be written to SERROR register (writing will clear the bit in SERROR register bit field) |  |
| sactive(var) | var: data read from SACTIVE register |  |
| satapm var | var: HIPM mode (1 : active, 2 : partial, 6 : slumber mode) | Supported only on ICH6R with int_ahci.drv |
| comreset var | var : reset mode (0 : port reset, 1 : HBA reset - all port) | int_ahci.drv supports comreset 0 & 1. int_ich.drv supports only comreset 1. |
| ahci 1/0 | ahci 0 : Standard ATA mode (default) ahci 1 : AHCI mode | User must make a call to scanallpci and setha() after ahci command. |
| ncq 1/0 | Flag, to send ncq array command |  |
| clearncq | Clears ncq array | ncq flag =1 |
| sendncq 1/0 | Sends the ncq array queue Clears the ncq array sendncq 0: do not wait for command completion sendncq 1: wait for command completion | ncq flag =1 |

More to be done….

### Drive Commands

Before any drive command is issued, the user must make sure the controller is selected and the driver is loaded by issuing following two PCI functions

1 – scanpci     or    scanallpci

2 – setha(HA#)

For DMA functions/commands, the user must make sure the following are true:

- Controller supports DMA and/or UDMA

- Transfer mode is set by issuing setf(m) function

For Extended command, you must make sure your controller supports extended mode

[note] any drive command having CHS or LBA mode addressing option, to issue command in LBA mode, the user must issue “slba 1” prior to issuing the drive command. Or, if user wants to use CHS mode, you’ll are required to issue “slba 0” prior to issuing the drive command

The command execution timeout is based on the CMD_TIMEOUT global variable; the value is in milliseconds. User can modify the timeout value using cmdtimeout(exp) function.

ex: cmdtimeout(123);	// change cmd timeout value to 123 milliseconds

All drive commands will be affected.

| function syntax | OP | parameter/description |
| --- | --- | --- |
| cmd(op,fe,sc,sn,cl,ch,dh,bs,xb,dir) | user | Create and issue user defined drive command. User can use this function to issue Vendor Unique commands. op: drive opcode fe: feature (16bit) sc: sector count (16bit) sn: sector number (16bit) cl: cylinder low (16bit) ch: cylinder high (16bit) dh: device/head (16bit) bs: block size (32bit) xb: blocks to transfer (32bit) dir:data transfer direction (8bit) 0 – No data transfer 1 – Data in (from drive) 2 – Data out (to drive) [note] “bs” & “xb” has no meaning if “dir” is set to ZERO example: to unlock Samsung Drive void main() { int CMD_UNLOCK; int PASS_FE; int LOCK; CMD_UNLOCK = 0xC0; PASS_FE = 0x22; LOCK = 0; cmd(CMD_UNLOCK,PASS_FE,LOCK, 0,0,0,0xA1,0,0,0); } To set the |

By function name

| function syntax | OP | parameter/description | requirement |
| --- | --- | --- | --- |
| cfa_es(lba, s) | 0xC0 | CFA Erase sector lba: s: sector |  |
| dcfg(f) | 0xB1 | Device Configuration f: Feature 0xC0 – Restore 0xC1 – Freeze lock 0xC2 – Identify 0xC3 – Set |  |
| ckpw | 0xE5 | Check Power Mode |  |
| diag | 0x90 | Diagnostic |  |
| dreset | 0x08 | NA |  |
| dw fn | 0x92 | Download Micro Code (Diskware) fn: filename example: dw “palo.dn2”; |  |
| idle t | 0xE3 | Idle t: timer period value 0 // Timeout disabled 1-240 // (t * 5) seconds 241-251 // ((t-240)*30) minutes 252 // 21 minutes 253 // between 8 and 12 hours 254 // Reserved 255 // 21 min 15 seconds |  |
| flush | 0xE7 | Flush Cache |  |
| flushe | 0xEA | Flush Cache Extended |  |
| id m | 0xEC | Device Identify m: display mode 0 == Do not display data 1 == Display data |  |
| idlei | 0xE1 | Idle Immediate |  |
| nop | 0x00 | NA |  |
| nvcache(fea,lba,sc) | 0xB6 | Send Non-Volatile CACHE command to drive. Features register controls what type of NVCACHE command. 0x00 : Set NV Cache Power Mode 0x01 : RETURN From NV Cache Power Mode 0x10 : Add LBA(s) to NV Cache Pinned 0x11 : Remove LBA(s) From NV Cache Pinned Set 0x12 : Query NV Cache Pinned Set 0x13 : Query NV Cache Misses 0x14 : Flush NV Cache | For Hybrid-HDD |
| rbuf | 0xE4 | Read Buffer |  |
| reset | NA | reset device – issue soft reset to controller/drive |  |
| rd(c_lba, h, s, b) | 0x20 | Read sector - PIO c_lba: cylinder or lba h: head – valid if not in lba mode s: sector – valid if not in lba mode b: #of blocks to read |  |
| rde(lba, b) | 0x24 | Read sector extended – PIO lba : lba location to read b: #of blocks to read |  |
| rdlg (l,h,s) | 0x22 | Read Long l: cylinder or lba h: head s:sector | Id or init |
| rdle(l,s1,s2) | 0x2F | Read Log Extended l: logAddress s1: sector offset s2: sector count |  |
| rdma(a,h,s,b) | 0xC8 | Read DMA a: cylinder or lba h: head – valid if CHS mode enabled s: sector – valid if CHS mode enabled b: #of blocks to xfer | setf() |
| rdmae(lba, b) | 0x24 | Read DMA extended lba: lba location to read b: #of blocks to read | - setf() - Controller with DMA support |
| rdmaq(lba, b, tag) | 0xC7 | Read DMA Queued lba: b: #of blocks to xfer tag: tag id | - setf() - |
| rdmaqe(lba, b, tag) | 0x26 | Read DMA Queued extended lba: lba location to read b: #of blocks to read tag: tag id | - setf() - |
| rm(a,h,s,b) | 0xC4 | Read Multiple a: Cylinder or LBA h: head – valid if CHS mode enabled s: sector – valid if CHS mode enabled b: #of blocks to xfer | sm( ) |
| rme(lba, b) | 0x29 | Read Multiple Extended | Must have issued set multiple command |
| rnma | 0xF7 | Read Native Max Address |  |
| rnmae | 0x27 | Read Native Max Address Extended |  |
| rtsk | NA | read and display current device TF |  |
| rv(a,h,s,b) | 0x40 | Read Verify a: Cylinder or LBA h: head – valid only in CHS mode s: sector – valid only in CHS mode b: #of blocks to xfer |  |
| rve(lba,b) | 0x42 | Read Verify Extended lba: b: #of blocks to xfer |  |
| rw fn | 0x92 | Download Micro Code (Ramware) fn: filename example: rw “palo.dn2”; |  |
| scdp | 0xF6 | Security – Disable password |  |
| scep | 0xF3 | Security - Erase Prepare |  |
| sceu | 0xF4 | Security – Erase Unit |  |
| scfl | 0xF5 | Security – Freeze Lock |  |
| scsp | 0xF1 | Security - Set Password |  |
| scul | 0xF2 | Security - Unlock |  |
| serv | 0xA2 | Overlap * Queued service |  |
| setf(f) | 0xEF | Set Features f: Feature value 01h: Enable 8-bit data transfers 02h: Enable write cache 03h: Set transfer mode based on value in Sector Count register 33h: Disable retry 42h: Enable AAM 44h: Length of vendor specific bytes on READ LONG/WRITE LONG commands 54h: Set cache segments to Sector Count register value 55h: Disable read look-ahead feature 66h: Disable reverting to power on defaults 77h: Disable ECC 81h: Disable 8-bit data transfers 82h: Disable write cache 88h: Enable ECC 99h: Enable retries AAh: Enable read look-ahead feature ABh: Set maximum prefetch using Sector Count register value BBh: 4 bytes of vendor specific bytes on READ LONG/WRITE LONG commands C2h: Disable AAM CCh: Enable reverting to power on defaults f0h: disable dummy RG, VU f1h: disable s/w ecc function, VU f2h: disable defect management, VU f3h: disable offtrack write, VU f4h: Go back to non volatile capacity on hard reset fbh: Keep current volatile capacity on hard reset for Time's request fch: enable offtrack write, VU fdh: enable defect management, VU feh: enable s/w ecc function, VU ffh: enable dummy RG, VU 03h - Set Transfer mode in Sector Count Reg value 00h=PIO deflt, 01h=PIO deflt/disbl IORDY, 00001nnn=PIO w/ IORDY, 00100nnn=MW DMA TO Set mode setf(0x0003) Pio default mode setf(0x0103) Pio default mode, disable IORDY setf(0x0903) Pio flow control transfer mode 1 setf(0x0A03) Pio flow control transfer mode 2 setf(0x0B03) Pio flow control transfer mode 3 setf(0x2103) Multiword DMA mode 1 setf(0x2203) Multiword DMA mode 2 setf(0x2303) Multiword DMA mode 3 setf(0x4103) Ultra DMA mode 1 setf(0x4203) Ultra DMA mode 2 setf(0x4303) Ultra DMA mode 3 setf(0x4403) Ultra DMA mode 4 setf(0x4503) Ultra DMA mode 5 setf(0x4603) Ultra DMA mode 6 54h - Set cache segments to Sector Count Reg ABh - Set max prefetching using Sector Count Reg value For more detail for setting udma mode refer to section 6.1 |  |
| setp(param) | 0x91 | Set parameter Param: parameter |  |
| sk(a,h) | 0x70 | Seek a: Cylinder or LBA h: head – valid only in CHS mode |  |
| sleep | 0xE6 | Sleep |  |
| sm(m) | 0xC6 | Set Multiple m: multiple value |  |
| smart(f,opt1,opt2) | 0xB0 | Smart f: feature D0 – SMART Read Data ( SRAV ) D1 – SmartReadAttributeThresholds ( SRAT ) D2 – Enable/Disable Attrib ( SAAS (opt) ) D3 – SmartSaveAttributeValues ( SSAV ) D4 – Execute Off-line immediate ( SAST : abort self test) ( SCTC : Comprehensive test ) ( SCTO : Comprehensive test ) ( SEOI : Offline Immediate ) ( SQTC : Quick self test ) ( SQTO : Quick self test ) ( SSTC : Save attr value ) ( SSTO : Save attr value ) D5 – Read Log ( SRLS ( opt1, opt2 ) ) ( SRST : Read self test sec ) ( SRLC : Read Log Record ) D6 – Write Log ( SWLS ( opt1, opt2 ) ) ( SWST ( opt1, opt2 ) ) D7 – Obselete D8 – Enable operation ( SESO ) D9 – Disable operation ( SDSO ) DA – Return status ( SRSS ) DB – SmartEnableDisableAutoOffline ( SAOL(opt) ) DE – VU ( SISV ) opt1: option1 – used with D2, D5, & D6 This value sets the SectCount opt2: option2 – used with D4, D5, & D6 This value sets the SectNum |  |
| smax(f,mlba,f) | 0xF9 | Set Max Address f: feature 00 - Obsolete (I will use it for Set Max Address) 01 - Set Max Set password 02 - Set Max Lock 03 - Set Max Unlock 04 - Set Max Freeze lock mlba: max lba to set to f: flag 0 == volatile 1 == non-volatile |  |
| smaxe(mlba, flag) | 0x37 | Set Max Address Extended mlba: max lba flag: 0 == volatile 1 == non-volatile |  |
| stbi | 0xE0 | Standby Immediate |  |
| stby t | 0xE2 | Standby t: time perior value |  |
| stconfig(i,s,t,f) | 0x51 | Config Stream i: stream id s: size t: timeout f: feature option |  |
| strdma(i,s,t,l,f) | 0x2A | Read Stream DMA i: stream id s: size t: timeout value l: lba f: featureOption |  |
| strpio(i,s,t,l,f) | 0x2B | Read Stream PIO i: stream id s: size t: timeout value l: lba f: featureOption |  |
| stwdma(i,b,t,l,f) | 0x3A | Write Stream DMA i: stream id b: #of blocks to xfer t: timeout l: lba f: feature option |  |
| stwpio(i,b,t,l,f) | 0x3B | Write Stream PIO i: stream id b: #of blocks to xfer t: timeout l: lba f: feature option |  |
| wbuf | 0xE8 | Write Buffer |  |
| wdma(a,h,s,b) | 0xCA | Write DMA a: cylinder or lba h: head – valid if CHS mode enabled s: sector – valid if CHS mode enabled b: #of blocks to xfer |  |
| wdmae(lba,b) | 0x35 | Write DMA Extended lba: b: #of blocks to read |  |
| wdmafe(lba, b) | 0x3D | Write DMA FUA Extended lba: b: #of blocks to xfer |  |
| wdmaqfe(lba,b) | 0x3E | Write DMA Queued FUA Extended lba: b: #of blocks to xfer |  |
| wdmaq(lba,b,tag) | 0xCC | Write DMA Queued lba: b: #of blocks to xfer tag: tag id |  |
| wdmaqe(lba,b,tag) | 0x36 | Write DMA Queued Extended lba: b: #of blocks to read tag: tag id |  |
| wfldma(lba, nb, tagId) | 0x61 | Write First Party DMA tagId: cmd tag id lba: lba location to read nb: num of blocks to read |  |
| wm(a,h,s,b) | 0xC5 | Write Multiple a: Cylinder or LBA h: head – valid if CHS mode enabled s: sector – valid if CHS mode enabled b: #of blocks to xfer |  |
| wme(lba,b) | 0x39 | Write Multiple Extended lba: b: #of blocks to read |  |
| wmfe(lba, b) | 0xCE | Write Multiple FUA Extended lba: b: #of blocks to xfer |  |
| wr(a, h,s,b) | 0x30 | Write Sector – PIO a: Cylinder or LBA h: head – valid only in CHS mode s: sector – valid only in CHS mode b: #of blocks to read |  |
| wre(a,b) | 0x34 | Write Sector Extended a: Cylinder or LBA b: #of blocks to read |  |
| wtlg (l,h,s) | 0x32 | Write Long l: cylinder or lba h: head s:sector | Id or init |
| wrle(l,s1,s2) | 0x3F | Write Log Extended l: log address s1: sector offset s2: sector count |  |

### Drive Commands (Samsung VU Commands)

| function syntax | OP | parameter/description | requirement |
| --- | --- | --- | --- |
| unlk |  | Unlock VU mode |  |
| lock |  | Lock VU mode |  |
| snde |  | Send drive error code | none |
| config |  | Display drive’s VU data which includes zone table | “init” |
| r2b FID |  | Load code from Ref-MC to Boot location FID: MCFS file id | FW must support DL-PTR |
| r2mc FID |  | Copy code from Ref-MC to MC FID: MCFS file id | FW must support DL-PTR |
| mc2b(FID) |  | Load code from MC to Boot location FID: MCFS file id | FW must support DL-PTR |
| h2mc(filename,FID) |  | Load code from HOST to MC filename: file to download FID: MCFS file id | FW must support DL-PTR |
| Chrb val | 9Ah/17h | Read Channel Buffer [0-ffffh] |  |
| Chrp(val,RturnVal | 9Ah/1Ah | Read Channel Preamp [0-ffffh] returns the data on ReturnVal |  |
| Chrr(val,ReturnVal) | 9Ah/16h | Read Channel Register[0-ffffh], returns the data on ReturnVal |  |
| Chud |  | Read Channel Record none | Uses channel table in Buffer |
| Chwb val | 9Ah/15h | Write channel Buffer [0-ffffh] |  |
| chwp val | 9Ah/19h | Write channel Preamp [0-ffffh] |  |
| chwr val | 9Ah/14h | Write channel Register [0-ffffh] |  |
| clearncq | n/a | Clears ncq command queue | ncq flag=1 |
| conv val | 9Ah/1Eh | val = [0/1/2]0 = LBA to physical 1 = physical to LBA 2 = LBA to physical with defect mapping: Drive type/FW dependent val = [0/1/2] |  |
| filt (s,cyl) | C2h | Write filter register. The R/W channel registers are addressed through ASIC register 1032h S: sector number Cyl: cylinder |  |
| fmtu opt | 8Fh | Format Unit [options 0- 255] Defect List Utility 1.Create D list from the burn-in error log 2.Create R and S list from the D list. 3.Add the defect specified by the (C,H,S) to the A list. 4.Initialize the A list. 5.DC erase the Track. 9. Read Servo Writer Record | opt can be greater than 255. (LSB of opt : feature register, MSB of opt : sector count register) |
| fmtd opt | 8Ch | Format track with Defect [0/1] |  |
| fmtg | 8Dh | Format Gap |  |
| folw | FBh | Get PES distribution :test |  |
| getmodel(str1) |  | Puts model to str1 | Must do id/init first |
| getfw(str1) |  | Puts fw version into str1 | Must do id/init first |
| getsn(str1) |  | Puts serialnumber into str1 | Must do id/init first |
| getengver(str1) |  | Puts engineering firmware version into str1 | Must do init first |
| getmaxhead Var |  | Returns max head for current drive, |  |
| findlastcyl var |  | Returns last cylinder |  |
| getmaxzone var |  | Returns max zone |  |
| chs2pba var |  | Returns pba for current chs |  |
| cs2lba var |  | Returns lba for current chs |  |
| calczone var |  | Returns currentzone for current cyl, current head |  |
| calcwedge(wedge) |  | Returns current wedge number using current cylinder, head,sector. wedge: Returned Wedge number |  |
| getsect4cyl var |  | Returns sector number for current cylinder |  |
| floatcmp(floata,float b,int c) |  | Compares two float a and b and return c as the result. c == 1 if a is greater than b, c == 0 if a is equal to b, c == -1 if a is less than b. |  |
| str2float(str a,float b); |  | Changes string to a float String a: float in a string format Float b: a float number Example: float a; str2float(“1.0”,a); // a is equal to 1.0 |  |
| newlogfile “filename” |  | Set filename to the logfile instead of cube.log If filename = “serialnumber” Then the actual file name will be the serial number of the testing drive You will need to do identify before this command. Example: id 0; newlogfile “serialnumber”; logfile 1; |  |
| delfile “filename” |  | Deletes the file named filename |  |
| showstat |  | Replaces the previous command summ. Prints the status of read/write/seek count |  |
| zerostat |  | Replaces the previous command zero. Zeros out the read/write/seek count |  |
| Addh val |  | Adds the val the head, increments it until max head, then increments the cylinder until max cylinder for all head |  |
| Addc val |  | Adds the val to cylinder until the max cylinder |  |
| gettf(RegNum, ReturnVal); |  | GETTF -- Gets the taskfile register Parameter: int RegNum, int Val RegNum :1 ->returns the feature/Error register to Val RegNum :2 ->returns the Sector Count register to Val RegNum :3 ->returns the Sector Number register to Val RegNum :4 ->returns the Cylinder Low register to Val RegNum :5 ->returns the Cylinder High register to Val RegNum :6 ->returns the Device Head register to Val RegNum :7 ->returns the command/ Status register to Val default: returns 0 to Val example: gettf(1,R0);// R0 contains feature/error register value |  |
| gird | 9Ah/04h | Get Read Current |  |
| giwt | 9Ah/03h | Get Write Current |  |
| idto opt | 9Ah/0Eh | Idle Seek Timeout [Enable=1,Disable=0] |  |
| init zone | C0h/ECh | Initialize Drive Zone Limits [0-255] zn: zone id. If 0, init full user accessable zone This command will unlock the drive and retrieve VU specific info from the drive. It will also update MAX_PC, MAX_PH, MAX_PS, MAX_PBA, and MIN_PC |  |
| inith zn hd | C0h/ECh | Initialize Drive Zone Limits [zone][hd] zn: zone to init to sn+100 will set the c to max_cyl for that head hd: head to init to This command DOES NOT issue drive command. This will use zone table info retrieved by issuing “init” and will update MAX_PC, MAX_PS, MAX_PBA, and MIN_PC for zn & hd | “init” must have been issued for correct functionality |
| loadcompat | func | Loads the compat driver for dos cube |  |
| ltsk | func | Gets the last set of command taskfile |  |
| mput fid | 0x9A/0x22 | Write MCFS File (fid) |  |
| mget fid | 0x9A/0x22 | Read MCFS File [fid] |  |
| offt offset | FDh | Set track offset percentile ((0-31) |  |
| phrd sectorC | 80h | Physical Read Sectors (0-255) | Physical C/H/S should be set |
| phrv sectorC | 81h | Physical Read Verify Sectors (0-255) | Physical C/H/S should be set |
| phwr sectorC | 82h | Physical Write Sectors (0-255) | Physical C/H/S should be set |
| prdl sectorC | 22h | Physical version of ATA Read Long ( read 1 sector plus ECC bytes) | Must do set feature 0x44 and then id in order to use this command to set actual ECC # |
| prlu | 84h | Physical read long | Reads two sectors of data including ecc bytes |
| prtk | 86h | Physical Read Track | Physical C/H should be set |
| psek mode | 8Eh | Physical Seek (Mode: 0=write/1=read) | Physical C/H/S should be set |
| pwrl sectorC | 32h | Physical version of ATA Write Long ( write 1 sector plus ECC bytes) | Must do set feature 0x44 and then id in order to use this command to set actual ECC # |
| pwtk | 85h | Physical Write Track | Physical C/H/S should be set |
| rchd hd | 9Ah/0Ch | RCO test for specific Head [head 0-max] |  |
| rcoa hd | 9Ah/0Bh | RCO test for Drive | Generate RCO test for all zone s and heads |
| rczh zone | 9Ah/0Ah | RCO test for specific zone/Head[zone 0-max] |  |
| rczn zone | 9Ah/09h | RCO test for specific zone [zone 0-max] |  |
| Rdib | 1Ah | Read Bias Current | Currently calculated for agere only, more to come |
| Rdiw | 1Ah | Read write Current | Currently calculated for agere only, more to come |
| rdbf val | 88h | Read Buffer Block Page [page ffffh] |  |
| Rdhv | 9Ah/0Dh | Read Buffer Head Voltage |  |
| rdxr val | F0h | Read External Memory byte [0-ffffh] | The disk memory location [nn] is read ans displayed |
| rdxw (val,RtnVal) | 9Ah/11h | Read external memory word 2-bytes [mem location] RtnVal: value returned to use | The disk memory location [nn] is read ans displayed |
| Rpes | FBh | Read PES amplitude |  |
| scra | n/a | Servo calibration |  |
| Sendncq | n/a | Sends ncq commands to the driver | ncq flag=1 |
| sgry opt | FAh | Scan Grey Code: The 13 bit gray code at DSP memory address 0205h is read and displayed. The ACC is set equal to the 16 bit contents of DSP address 0205h. [0-255] |  |
| shrr opt | FFh/80h | Set Hidden Retry count – Read [0-10] |  |
| shrw opt | FFh/C0h | Set Hidden Retry count – Write [0-10] |  |
| sird current | 9Ah/02h | Set Read channel Current [current] | Uses current cylinder/Head |
| siwt current | 9Ah/01h | Set Write channel Current [10h-98h] | Uses current cylinder/head |
| Skew | F7h | Head skew calibration |  |
| test | 9Ah | Create and issue user defined vendor unique drive command. Subop: drive subopcode (8 bit) sc: sector count (16bit) sn: sector number (16bit) cl: cylinder low (16bit) ch: cylinder high (16bit) dh: device/head (16bit) |  |
| tnmr (repeat, pass) | 9Ah/05h | Tune MR Head [repeat count 1-255] [pass] |  |
| tone val | 8Ah | Tone Fill Gap |  |
| wrtc current |  | Set Write current value [0-ffh] |  |
| wrxr val |  | Write External Register(byte)[0-ffffh] |  |
| wrxw (address,val) |  | Write external Register(word)[0-ffffh] Address: Register address Val: value |  |
| wtrk val |  | Write Track(starting sector)[0 – 255] | The command argument specifies the starting sector to write. All sectors of the track are written starting at the sector number[nn]. |
| wrbf val | 0x89 | Write buffer block [0-0xffff] |  |

### MISC commands (Math,Test….)

| function syntax | OP | parameter/description | requirement |
| --- | --- | --- | --- |
| Sqrt(val,RtnVal) |  | Val: value to be square rooted RtnVal: Value returned | Val , and RtnVal is both type float |
| log(val, RtnVal) |  | Val: value to be log RtnVal: Value returned | Val , and RtnVal is both type float |
| log10(val, RtnVal) |  | Val: value to be log10 RtnVal: Value returned | Val , and RtnVal is both type float |
| sktm(mode) |  | 1. mode: 0=write/1=read) 2. “s” should be set up as test type. TRK_TRK 0x01 TWO_TRK 0x02 ONE_THIRD 0x04 FULL_TRACK 0x08 AVG_SEEK 0x10 WEIGHTED_AVG_SEEK 0x20 All test 0xff 3. “acc” should be set up as repeat count when we test WEIGHTED_AVG_SEEK. |  |
| showdefect(“filename”) |  | Displays the defect list to the file :filename | Must use after burin in |
| createfile(handle, name) |  | The createfile function creates or opens a file, directory, physical disk, volume, console buffer, tape drive, communications resource, mailslot, or pipe. - parameter / description @ handle: Variable to contain an open handle to the specified file. @ name: Pointer to a null-terminated string that specifies the name of the object to create or open. - warning : This function can damage your hard disk drive if you use it for a wrong purpose. |  |
| closehandle(handle) |  | The closehandle function closes an open object handle. - parameter / description @ handle: Handle to an open object. - warning : This function can damage your hard disk drive if you use it for a wrong purpose. |  |
| readfile(handle, lba, count) |  | The readfile function reads data from a file, starting at the position indicated by the lba. - parameter / description @ handle: Handle to the file to be read. @ lba : File LBA position to be read. @ count : Number of sectors to be read from the file. - warning : This function can damage your hard disk drive if you use it for a wrong purpose. |  |
| writefile(handle, lba, count) |  | writefile function writes data to a file. - parameter / description @ handle: Handle to the file to be written. @ lba : File LBA position to be written. @ count : Number of sectors to be written from the file. - warning : This function can damage your hard disk drive if you use it for a wrong purpose. |  |

### Command compatibility between Gemini and Cube

| Gemini commands | Cube Commands |  |
| --- | --- | --- |
| summ | showstat |  |
| zero | zerostat |  |
| ldac | N/A This is obsolete for cube, since cube have more than one parameters | Example: Ldac 9; wtrg f2h; fmtu 3; Do cmd(0x8f,3,9,0,0,0,512,1,0); |
| wtrg | Use cmd to input the register value see example below | Example: Ldac 9; wtrg f2h; fmtu 3; Do cmd(0x8f,3,9,0,0,0,512,1,0); |
| spsz | tnmr |  |

### Error code definition

| Error code | Error Number | Definition |
| --- | --- | --- |
| EC_NOERROR | 0x00 | Pass, no error |
| EC_ERROR | 0x01 | Error, undefined |
| EC_KEYBOARD_INTERRUPTION | 0x02 | Keyboard interruption |
| EC_ERRORHALT | 0x03 | Error halt, set by the user |
| EC_FAILED_TO_OPEN_LOGFILE | 0x04 | Failed to open logfile |
| EC_CMD_FAIL_TO_OPEN_FILE | 0x05 | Fail to open file |
| EC_CMD_FAIL_TO_READ_FILE, | 0x06 | Fail to read file |
| EC_CMD_FAIL_TO_WRITE_FILE, | 0x07 | Fail to write file |
| EC_CMD_FAIL_IDENTIFY_DRIVE, | 0x08 | Failed to identify the drive |
| EC_BUFFER_MISCOMPARE | 0x2000 | Buffer miscompare |
| EC_ALLOC_MEMORY | 0x4000 | Cannot allocate memory |
| EC_ALLOC_BUF1 | 0x4001 | Cannot allocate buffer 1 |
| EC_ALLOC_BUF2 | 0x4002 | Cannot allocate buffer 2 |
| EC_ALLOC_BUF3 | 0x4003 | Cannot allocate buffer 3 |
| EC_DRIVER_NOT_LOADED | 0x4004 | Driver not loaded |
| EC_DRIVER_NO_SETHA | 0x4005 | Driver User has yet to issue SETHA |
| EC_DRIVER_NO_HOST_ADAPTER | 0x4006 | Driver No host adaptor found |
| EC_DRIVER_NO_STATUS | 0x4007 | Driver No Status found |
| EC_DRIVER_FAILED_TO_RESET | 0x4008 | Driver Failed to reset |
| EC_DRIVER_FAILED_TO_ABORT | 0x4009 | Driver Failed to abort |
| EC_DRIVER_FAILED_TO_OPEN_FILE | 0x4010 | Driver Failed to open file |
| EC_DRIVER_WRONG_FILE_FORMAT | 0x4011 | Driver Wrong file format |
| EC_DRIVER_FAILED_TO_READ_FILE | 0x4012 | Driver Failed too read driver file |
| EC_DRIVER_FILE_ID_NOT_FOUND | 0x4013 | Driver File Id not found |
| EC_DRIVER_FILE_LENGTH_ZERO | 0x4014 | Driver File Length is zero |
| EC_DRIVER_FILE_ACCESS | 0x4015 | Driver no file access |
| EC_DRIVER_FAILED_TO_ALLOCATE_MEM | 0x4016 | Driver failed allocate memory |
| EC_DRIVE_MCFS_ERROR | 0x6000 | Mcfs error |
| EC_DRIVE_MCFS_READ_FAILED | 0x6001 | MCFS read failed |
| EC_DRIVE_MCFS_WRONG_SPT | 0x6002 | MCFS wrong script |
| EC_DRIVE_ERROR | 0x8000 | Drive Error |
| EC_DRIVE_CMD_TIMEOUT | 0x8001 | Command timeout |
| EC_DRIVE_DRQ_TIMEOUT | 0x8002 | DRQ timeout |
| EC_DRIVE_IRQ_TIMEOUT | 0x8003 | IRO timeout |
| EC_DRIVE_BUSY_TIMEOUT | 0x8004 | Busy timeout |
| EC_DRIVE_HOST_RESET_TIMEOUT | 0x8005 | Host Reset Time Out |
| EC_DRIVE_ST_WRITE_FAULT | 0x8006 | Status Write fault error |
| EC_DRIVE_ST_NOT_READY | 0x8007 | Status Drive not ready |
| EC_DRIVE_ST_SEEK | 0x8008 | Status Seek error |
| EC_DRIVE_ST_DATA_CORRECTED | 0x8009 | Status Data corrected |
| EC_DRIVE_ST_BUSY | 0x8010 | Status busy |
| EC_DRIVE_ER_SECTOR | 0x8011 | Error Reg sector |
| EC_DRIVE_ER_ECC | 0x8012 | Error Reg ECC |
| EC_DRIVE_ER_UNDEFINED | 0x8013 | Error Reg undefined |
| EC_DRIVE_ER_ID_NOT_FOUND | 0x8014 | Error Reg ID not found |
| EC_DRIVE_ER_ABORT_COMMAND | 0x8015 | Error Reg abort command |
| EC_DRIVE_ER_SEEK | 0x8016 | Error Reg seek error |
| EC_DRIVE_ER_ADDRESS_MARK | 0x8017 | Error Reg Address Mark not found |
| EC_CMDQ_TOO_MANY_ENTRY | 0x8018 | CommandQ Too Many Entry |
| EC_CMDQ_TAG_NOT_FOUND | 0x8019 | CommandQ Tag not found |
| EC_DOWNLOAD_INVALID_FLASH_ID | 0x8020 | Download invalid Flash ID |
| EC_DOWNLOAD_DATA_MISCOMPARE | 0x8021 | Download Data Miscompare |
| EC_DOWNLOAD_WRONG_MODE | 0x8022 | Download Wrong mode |
| EC_DRIVE_BUSY_NOT_CLR | 0x8023 | Drive busy not clear |

## Using CUBE

fig 8-1

(Cube console window)

Assuming Hardware & Software requirement is met, start the CUBE and you will see a screen similar to fig 8-1.

By default, at the CUBE load time, it will load Compat.DRV. Default driver loaded will run on on-board interface connector.

### Setting-up test environment by selecting the controller

Before the users of CUBE can exercise the drive, you must setup the controller first. To do this, please follow the following steps (if default driver is not desired):

Step1:  scan for the PCI controller card by issuing

> scanpci		// If your card is not found, issue scanallpci command

// See fig 8-2

fig 8-2

(scanning for Controller)

Step2: Load appropriate driver by issuing

> setha(0)		// To load and setup for controller Intel ATA(ICH4)

// See fig 8-3

fig 8-3

(Selecting Controller)

Once the controller is selected and appropriate driver is loaded, the user can now issue commands to drive.

Commands can be issued from the command-line, or you can load pre-written Small-C script and run. To load and run, do the following

- load myscript		// loads script call “myscript”

- run			// If the script was loaded successfully, test will start

### CUBE Test Script Examples

#### Sequential Seek Time Measurement:

void DoSequantialSeek();

void main(void)

{

int counter;

cwin(5);         // Create User defined console window

id(1);           // Issue Identify

cputs(1,1,"Sequantial Seek Test", 0x20);

DoSequantialSeek();

}

void DoSequantialSeek()

{

int c, h;

int totalTime;

slba 0;			// Disable LBA addressing mode

cmdtime 1;		// Enable command time measuring clock

//----------------------------------------------

//- Do Sequential seek (all cyl, then heads)

//----------------------------------------------

for(h=0; h<2;h++)	// Head loop

{

totalTime=0;		// Initialize totalTime

for(c=0; c< 1000; c++)	// We will seek from C=0 to 1000

{

sk(c, h);		// Seek

totalTime = totalTime+CMD_TIME;	// Accumulate test time

}

cputd(30,h,"SingleTrackSeek: %d  microsec", totalTime/c, 0x60);

}

return;

}

#### Random Seek Time Measurement:

void DoRandomSeek(int loopCount);

void main(void)

{

int counter;

cwin(5);         // Create User defined console window

id(1);           // Issue Identify

cputs(1,1,"Random Seek Time Test", 0x20);

DoRandomSeek(1000);	// Do 1000 Random seeks

}

void DoRandomSeek(int loopCount)

{

int c, h;

int i;

int totalTime;

totalTime = 0;

randomize;			// Randomize

cmdtime 1;			// Enable the clock(microsecond clock

slba 1;

for(i=0;i<loopCount;i++)

{

cputd(5,4,"%ld",i, 0x35);	// Show loop count

rand(R0, 0, MAX_LBA);	 	// Generate random LBA

sk(R0, 1);				// Seek

totalTime=totalTime+CMD_TIME;	// Accumulate the total time

}

cputd(30,4,"RandomSeekTime: %d usec", totalTime/loopCount, 0x60);

return;

}

#### Do Sequential DMA Write/Read:

void main()

{

int lba;

int startLBA;

id(1);			// Identify

erhlt 1;			// Enable error halt (halt when error occurs

slba 1;			// Enable LBA addressing mode

bcmp 1;			// Enable Buffer compare when data is read

wfill(0x12345678);	// Fill write buffer with pattern 0x12345678

MAX_LBA = MAX_LBA - 1000;// when id(1) is called, MAX_LBA was set

startLBA = 0;

putd("MAX_LBA = %ld", MAX_LBA); newline;

setf(0x2203);			// Set transfer mode to DMA mode 2

time;newline;date;newline;	// Time stamp

for(lba=startLBA; lba < MAX_LBA; lba = lba+255)

{

wdma(lba, 0, 0, 255);	// Write DMA

}

setf(0x2103);			// Set transfer mode to DMA mode 1

time;newline;date;newline;	// Time stamp

for(lba=startLBA; lba < MAX_LBA; lba = lba+255)

{

wdma(lba, 0, 0, 255);	// Write DMA

}

time;newline;date;newline;	// Time stamp

for(lba=startLBA; lba < MAX_LBA; lba=lba+255)

{

rdma(lba, 0, 0, 255);	// Read DMA – data compare will be

//    done since we set the dcmp 1

}

time;newline;date;newline;	// Time stamp

return;

}

#### Do Sequential UDMA Write/Read:

void main()

{

int lba;

int startLBA;

id(1);			// Drive identify

erhlt 1;			// Enable error halt

slba 1;			// Enable LBA mode addressing

wfill(0x12345678);	// Fill Write buffer with pattern 0x12345678

MAX_LBA = MAX_LBA - 1000;

startLBA = 0;

putd("MAX_LBA = %ld", MAX_LBA); newline;

setf(0x4403);		// Set transfer mode to UDMA mode 4

time;newline;date;newline;

for(lba=startLBA; lba < MAX_LBA; lba = lba+255)

{

wdma(lba, 0, 0, 255);	// Do UDMA Write

}

setf(0x4503);		// Set transfer mode to UDMA mode 5

time;newline;date;newline;

for(lba=startLBA; lba < MAX_LBA; lba = lba+255)

{

wdma(lba, 0, 0, 255);	// Do UDMA Write

}

time;newline;date;newline;

for(lba=startLBA; lba < MAX_LBA; lba=lba+255)

{

rdma(lba, 0, 0, 255);	// Do UDMA Read – do buffer compare

//	since we enabled bcmp 1

}

time;newline;date;newline;

return;

}

#### Legacy Command Queuing:

//=================================================

//= By: Daniel

//=

//=     Tag Cmd Queue example using CUBE

//=

//=================================================

void main(void)

{

int tag1, lba;

id(0);                   // Device identify

trace 1;                // Turn on TRACE (for debugging)

cmdtime 1;              // Enable cmd time measurement

//    (to see execution time)

for (tag1=1; tag1<10; )    // for tag ID 1 to 30

{

rand(R0, 0, MAX_LBA); // Obtain random LBA

rdmaq(R0,1,tag1);      // Issue ReadCmdQ

tag1++;

}

for (R0=10; R0; R0--)

{

delaym(500);          // Wait for 500 milliseconds

checkq;               // Check to see whether we have any

//   outstanding cmdq that needs

//   servicing. If so, checkq will

//   service it

}

showq;  // see if anything is left in the Q

// If so, it means not all command was serviced

return;

}

# VTOOL

## Overview

This is overview of VTOOL Windows version. This document doesn’t explain the whole of VTOOL usage. This just explains how we can run VTOOL inside W-Cube and how we can run each menu.

W-Cube includes Windows version of VTOOL. It’s almost similar to Dos version of VTOOL. When we click “VTOOL” button, VTOOL menu tree will appear inside W-Cube as follows.

Before we click “VTOOL” button, we should connect a drive. If not, we can see some kind of error message.

Now we can expand each VTOOL directory as follows.

Now we can click “DEFECT” menu, and then we can watch Defect Statistical Chart as follows.

If we want to save this data, just hit F9 key and enter appropriate file name.

[NOTE] We can open multiple lists in Windows 2000, XP at the same time.

But we cannot open multiple lists in Windows 98, ME at the same time.

And if we select “SPAT” menu, we can run SPAT test.

To start test, just click “RUN” button.

There are two ways of saving a screen.

- To save whole test screen.

  - Select the “Capture” menu and select the “Window” sub-menu.

- To save the selected area.

  - Drag a mouse to select the area to capture.

  - Select the “Capture” menu and select the “Selection” sub-menu or press “Ctrl+C”.

[NOTE] Now, W-Cube supports jpg, gif, bmp file format. To decide which file format we save a screen as, we just enter appropriate file extension.

## Configuration

Windows VTOOL has some kinds of configuration option. To change them, we can use configuration dialog box. We can find it in a sub-menu of W-Cube.

Here we can change “MC Access Mode”, some kinds of operation option, identify the drive under testing, send reset to it.

[NOTE] MC Access Mode

a. DISK I/O

This is default I/O mode. In this mode, VTOOL communicate the drive directly to read M/C data.

b. MCF I/O

When we select this mode, we need to specify MCF file which was made from “M/C DATA – DISK TO MCF” menu. In this mode, VTOOL communicate the file to read M/C data instead of reading DRIVE directly.

c. FILE I/O

In this mode, VTOOL use separate files to read M/C data. This mode is for VTOOL debugging.

[NOTE] Windows VTOOL supports MCF file and MCF mode. It’s similar to Dos version MCR file but the file format is different.

## VTOOL API Layer

We can run almost VTOOL functions in W-CUBE command line.

### Functions

#### vtoolgetdata : gather specified data and save it into file.

1. Syntax: vtoolgetdata(func, directory_name, file_name);

2. parameters :

a. func : function name in VTOOL menu.

"" to remove the specified file.

b. directory_name : directory name for output file.

"" to use a serial number of connected drive.

c. file_name : output file name.

"" to use a serial number of connected drive.

Using the existing file name, new output will be added to it.

The list of functions which aren’t supported is as follows.

  - All functions under M/C DATA

  - All functions under VISUAL TEST

And VTOOL API layer has following special functions.

a. "GET_DLIST_MAP" : Capture D-List map.

b. "GET_VLIST_MAP" : Capture V-List map.

c. "GET_ELOG_MAP"  : Capture E-Log map.

d. “RUN_SPAT” : Run SPAT & capture the screen.

e. “RUN_TET” : Run TET & capture the screen.

#### vtoolstepmask : select or deselect Burn-in step mask.

1. Syntax:	vtoolstepmask(mode, step);

2. Parameters :

a. mode

0 to select a step

1 to deselect a step

2 to select all step

3 to deselect all step

b. step

if mode is 0 or 1, this is step to add or remove.

### Examples

1. vtoolgetdata("ANALYSIS\DEFECT", "", "_DMAP.TXT");

// Save “ANALYS\DEFECT” into “serialnumber\_DMAP.TXT”.

2. vtoolgetdata("ANALYSIS\DEFECT", ".", "");	// “.” means the current directory.

// Save “ANALYSIS\DEFECT” into “serialnumber.txt”

3. vtoolgetdata("GET_ELOG_MAP", "", "ELOG.GIF");

// Before we run this, we should set up all environment such as B/I step mask.

4. SPAT

void main()

{

R0 = 100;	// Cylinder

R1 = 0;	// Head

R2 = 0;	// Offtrack

R3 = 1000;	// Iteration

R4 = 200;	// Src Cyl

R5 = 0;	// Src Head

R6 = 10;	// Interval

R7 = 10;	// # of Cyl

R8 = 0;	// Type : Following(0), Random(1), Indicate(2), Rand Indicate(3), Seq Following(4)

R9 = 1;	// Mode : Read(2), Write(1), Real Write(5)

R10 = 0;	// TraceData : PERR(0), PRAW(1), USER(2)

R11 = 1;	// Srv RCC : OFF(0), ON(1)

R12 = 0;	// FFT Avg : TIME(0), FREQ(1)

R13 = 0;	// FFT Axis : Lin(0), dB(1)

R14 = 0;	// Reserved

R15 = 0;	// Reserved

R16 = 0;	// Reserved

R17 = 0;	// Reserved

R18 = 0;	// Reserved

R19 = 0;	// Reserved

vtoolgetdata("RUN_SPAT", "", "SPAT.GIF");

return;

}

5. TET

void main()

{

R0 = 100;	// Cylinder

R1 = 0;	// Head

R2 = 1;	// Sector

R3 = 1; 	// Step

R4 = 0;           // User Retry

R5 = 0;	// HR Retry

R6 = 5;	 // Read #

R7 = 40;	// Max offt

R8 = 130;	// Cell #

R9 = 0;	// ECC

R10 = 0;	// Adjacent Track

R11 = 1;	// DataPtn

R12 = 0;	// Reserved

R13 = 0;	// Reserved

R14 = 0;	// Reserved

R15 = 0;	// Reserved

R16 = 0;	// Reserved

R17 = 0;	// Reserved

R18 = 0;	// Reserved

R19 = 0;	// Reserved

vtoolgetdata("RUN_TET", "", "TET.GIF");

return;

}

6. Saving all data as separate files in a directory named as serial number.

void main()

{

vtoolstepmask(2, 0);	// select all step.

vtoolgetdata("GET_ELOG_MAP", "", "ELOG.GIF");

vtoolgetdata("GET_VLIST_MAP", "", "VLIST.GIF");

vtoolgetdata("GET_DLIST_MAP", "", "DLIST.GIF");

vtoolgetdata("", "", "_DMAP.TXT");	// delete existing output file.

vtoolgetdata("ANALYSIS\DEFECT", "", "_DMAP.TXT");

vtoolgetdata("", "", "_RESULT.TXT");

vtoolgetdata("ANALYSIS\BURN-IN RESULT", "", "_RESULT.TXT");

vtoolgetdata("", "", "_WHT.TXT");

vtoolgetdata("ANALYSIS\WEAK HEAD TEST RESULT", "", "_WHT.TXT");

vtoolgetdata("", "", "_STEPT.TXT");

vtoolgetdata("ANALYSIS\BURN-IN STEP TIME", "", "_STEPT.TXT");

vtoolgetdata("", "", "_STEP.TXT");

vtoolgetdata("ANALYSIS\BURN-IN STEP", "", "_STEP.TXT");

vtoolgetdata("", "", "_SMART.TXT");

vtoolgetdata("ANALYSIS\SMART RESULT", "", "_SMART.TXT");

vtoolgetdata("", "", "_SELOG.TXT");

vtoolgetdata("ANALYSIS\SMART ERROR LOG", "", "_SELOG.TXT");

vtoolgetdata("", "", "_MNT.TXT");

vtoolgetdata("ANALYSIS\PARAMETER MONITORING", "", "_MNT.TXT");

vtoolgetdata("", "", "_BISCRT.TXT");

vtoolgetdata("VIEW/EDIT LIST\BURN-IN SCRIPT\VIEW BURNIN SCRIPT", "", "_BISCRT.TXT");

vtoolgetdata("", "", "_CHNT.TXT");

vtoolgetdata("VIEW/EDIT LIST\R/W CHANNEL MENU\CHANNEL TABLE 1 [CHN_TBL ]\R/W CHANNEL TABLE", "", "_CHNT.TXT");

vtoolgetdata("", "", "_MATRIX.TXT");

vtoolgetdata("VIEW/EDIT LIST\R/W CHANNEL MENU\CHANNEL TABLE 1 [CHN_TBL ]\R/W CHANNEL MATRIX", "", "_MATRIX.TXT");

vtoolgetdata("", "", "_PMP.TXT");

vtoolgetdata("VIEW/EDIT LIST\R/W CHANNEL MENU\CHANNEL TABLE 1 [CHN_TBL ]\R/W PREAMP VALUES", "", "_PMP.TXT");

vtoolgetdata("", "", "_CHNV.TXT");

vtoolgetdata("VIEW/EDIT LIST\R/W CHANNEL MENU\CHANNEL TABLE 1 [CHN_TBL ]\R/W CHANNEL VALUES", "", "_CHNV.TXT");

vtoolgetdata("", "", "_FIRV.TXT");

vtoolgetdata("VIEW/EDIT LIST\R/W CHANNEL MENU\CHANNEL TABLE 1 [CHN_TBL ]\R/W FIR VALUES", "", "_FIRV.TXT");

vtoolgetdata("", "", "_SERR.TXT");

vtoolgetdata("VIEW/EDIT LIST\SORTED ERROR LOG", "", "_SERR.TXT");

vtoolgetdata("", "", "_SERVO.TXT");

vtoolgetdata("VIEW/EDIT LIST\SERVO INFORMATION", "", "_SERVO.TXT");

vtoolgetdata("", "", "_DSBER.TXT");

vtoolgetdata("VIEW/EDIT LIST\ERROR RATE TEST RESULT\Zone Error Rates (First)", "", "_DSBER.TXT");

vtoolgetdata("", "", "_2NDBER.TXT");

vtoolgetdata("VIEW/EDIT LIST\ERROR RATE TEST RESULT\Zone Error Rates (Second)", "", "_2NDBER.TXT");

vtoolgetdata("", "", "_10SBER.TXT");

vtoolgetdata("VIEW/EDIT LIST\ERROR RATE TEST RESULT\Zone Error Rates (Third)", "", "_10SBER.TXT");

vtoolgetdata("", "", "_MRTUNE.TXT");

vtoolgetdata("VIEW/EDIT LIST\MR TUNE LOG DATA", "", "_MRTUNE.TXT");

vtoolgetdata("", "", "_747TPI.TXT");

vtoolgetdata("VIEW/EDIT LIST\VIEW TPI 747 RESULT\TPI LOG from [TPI_WRW ]", "", "_747TPI.TXT");

vtoolgetdata("", "", "_BPICSM.TXT");

vtoolgetdata("VIEW/EDIT LIST\BPI RESULT\BPI CSM RESULT", "", "_BPICSM.TXT");

vtoolgetdata("", "", "_GEOM.TXT");

vtoolgetdata("VIEW/EDIT LIST\CURRENT GEOMETRY", "", "_GEOM.TXT");

vtoolgetdata("", "", "_NPV.TXT");

vtoolgetdata("VIEW/EDIT LIST\NPV TEST", "", "_NPV.TXT");

vtoolgetdata("", "", "_SPIKE.TXT");

vtoolgetdata("VIEW/EDIT LIST\AMPLITUDE SPIKE TEST", "", "_SPIKE.TXT");

vtoolgetdata("", "", "_SDLST.TXT");

vtoolgetdata("VIEW/EDIT LIST\SERVO DEFECT LIST", "", "_SDLST.TXT");

vtoolgetdata("", "", "_TDLST.TXT");

vtoolgetdata("VIEW/EDIT LIST\TRACK DEFECT LIST", "", "_TDLST.TXT");

vtoolgetdata("", "", "_DLIST.TXT");

vtoolgetdata("VIEW/EDIT LIST\PRIMARY DEFECT LIST", "", "_DLIST.TXT");

vtoolgetdata("", "", "_ARLIST.TXT");

vtoolgetdata("VIEW/EDIT LIST\AUTO REASSIGN LIST", "", "_ARLIST.TXT");

vtoolgetdata("", "", "_TA.TXT");

vtoolgetdata("VIEW/EDIT LIST\TA DEFECT LIST", "", "_TA.TXT");

vtoolgetdata("", "", "_SN.TXT");

vtoolgetdata("VIEW/EDIT LIST\DRIVE SERIAL NUMBER", "", "_SN.TXT");

}

Example script 2) Saving all data as a file named as serial number.

void main()

{

vtoolgetdata("", ".", "");		// delete existing output file.

vtoolgetdata("ANALYSIS\DEFECT", ".", "");

vtoolgetdata("ANALYSIS\BURN-IN RESULT", ".", "");

vtoolgetdata("ANALYSIS\WEAK HEAD TEST RESULT", ".", "");

vtoolgetdata("ANALYSIS\BURN-IN STEP TIME", ".", "");

vtoolgetdata("ANALYSIS\BURN-IN STEP", ".", "");

vtoolgetdata("ANALYSIS\SMART RESULT", ".", "");

vtoolgetdata("ANALYSIS\SMART ERROR LOG", ".", "");

vtoolgetdata("ANALYSIS\PARAMETER MONITORING", ".", "");

vtoolgetdata("VIEW/EDIT LIST\BURN-IN SCRIPT\VIEW BURNIN SCRIPT", ".", "");

vtoolgetdata("VIEW/EDIT LIST\R/W CHANNEL MENU\CHANNEL TABLE 1 [CHN_TBL ]\R/W CHANNEL TABLE", ".", "");

vtoolgetdata("VIEW/EDIT LIST\R/W CHANNEL MENU\CHANNEL TABLE 1 [CHN_TBL ]\R/W CHANNEL MATRIX", ".", "");

vtoolgetdata("VIEW/EDIT LIST\R/W CHANNEL MENU\CHANNEL TABLE 1 [CHN_TBL ]\R/W PREAMP VALUES", ".", "");

vtoolgetdata("VIEW/EDIT LIST\R/W CHANNEL MENU\CHANNEL TABLE 1 [CHN_TBL ]\R/W CHANNEL VALUES", ".", "");

vtoolgetdata("VIEW/EDIT LIST\R/W CHANNEL MENU\CHANNEL TABLE 1 [CHN_TBL ]\R/W FIR VALUES", ".", "");

vtoolgetdata("VIEW/EDIT LIST\SORTED ERROR LOG", ".", "");

vtoolgetdata("VIEW/EDIT LIST\SERVO INFORMATION", ".", "");

vtoolgetdata("VIEW/EDIT LIST\ERROR RATE TEST RESULT\Zone Error Rates (First)", ".", "");

vtoolgetdata("VIEW/EDIT LIST\ERROR RATE TEST RESULT\Zone Error Rates (Second)", ".", "");

vtoolgetdata("VIEW/EDIT LIST\ERROR RATE TEST RESULT\Zone Error Rates (Third)", ".", "");

vtoolgetdata("VIEW/EDIT LIST\MR TUNE LOG DATA", ".", "");

vtoolgetdata("VIEW/EDIT LIST\VIEW TPI 747 RESULT\TPI LOG from [TPI_WRW ]", ".", "");

vtoolgetdata("VIEW/EDIT LIST\BPI RESULT\BPI CSM RESULT", ".", "");

vtoolgetdata("VIEW/EDIT LIST\CURRENT GEOMETRY", ".", "");

vtoolgetdata("VIEW/EDIT LIST\NPV TEST", ".", "");

vtoolgetdata("VIEW/EDIT LIST\AMPLITUDE SPIKE TEST", ".", "");

vtoolgetdata("VIEW/EDIT LIST\SERVO DEFECT LIST", ".", "");

vtoolgetdata("VIEW/EDIT LIST\TRACK DEFECT LIST", ".", "");

vtoolgetdata("VIEW/EDIT LIST\PRIMARY DEFECT LIST", ".", "");

vtoolgetdata("VIEW/EDIT LIST\AUTO REASSIGN LIST", ".", "");

vtoolgetdata("VIEW/EDIT LIST\TA DEFECT LIST", ".", "");

vtoolgetdata("VIEW/EDIT LIST\DRIVE SERIAL NUMBER", ".", "");

vtoolgetdata("GET_DLIST_MAP", "", "DLIST.GIF");

vtoolgetdata("GET_VLIST_MAP", "", "VLIST.GIF");

vtoolgetdata("GET_ELOG_MAP", "", "ELOG.GIF");

}

---------------------------------end of file--------------------------------------

# Text boxes

2.

3.